## Slide 1: Wireless Networking
Ambuj Varshney
Assistant Professor, National University of Singapore
Wireless, Embedded Intelligence, Sensing, and Emerging Technologies Group
ambujv@nus.edu.sg

## Slide 2
Administration and Course Logistics

## Slide 3: Assignment 3a (no assignment 3b)
Link: https://weiserlab.github.io/ambuj/cs4222_assignment3a
Deadline :2nd of April 2023/ CANVAS submission page is live
Covers: 13% of overall grade
Wireless measurements using RSSI
No Plagiarism! We will check for code similarity
  No ChatGPT for this assignment
Notes: ++ We may all have heard of the term Internet of Things. So how are these wireless embedded systems related to the Internet of Things: Today, IoT includes a broad class of devices, including powerful platforms such as smartphones. However, it also includes more resource-constrained devices and what we call Wireless Embedded Systems, and in fact, I consider it to be one of the essential parts of the IoT ecosystem.
++ These are platforms equipped with a radio transceiver, sensor, microcontroller, and some form of energy storage. These platforms also often form a network, and sensor network as it is called has been an active area of research for the past two decades.
++ The research community has also developed wireless embedded platforms which we may know about, and these include: CMUCAM, which is an image sensor platform developed at Carnegie Mellon University, or Permamote is long life sensor platform from the lab I am associated with at UC Berkeley or Lorea which is a long-range backscatter platform that I had developed as part of my doctoral dissertation at Uppsala University. All of these are an example of Wireless Embedded Systems.

## Slide 4: Project
We decided to integrate some aspects of assignment 3b with Project
Deadline: 21st April 2023/ With penalty (10%) 28th April 2023
Should be done in a group
Notes: ++ We may all have heard of the term Internet of Things. So how are these wireless embedded systems related to the Internet of Things: Today, IoT includes a broad class of devices, including powerful platforms such as smartphones. However, it also includes more resource-constrained devices and what we call Wireless Embedded Systems, and in fact, I consider it to be one of the essential parts of the IoT ecosystem.
++ These are platforms equipped with a radio transceiver, sensor, microcontroller, and some form of energy storage. These platforms also often form a network, and sensor network as it is called has been an active area of research for the past two decades.
++ The research community has also developed wireless embedded platforms which we may know about, and these include: CMUCAM, which is an image sensor platform developed at Carnegie Mellon University, or Permamote is long life sensor platform from the lab I am associated with at UC Berkeley or Lorea which is a long-range backscatter platform that I had developed as part of my doctoral dissertation at Uppsala University. All of these are an example of Wireless Embedded Systems.

## Slide 5: Tutorials
Mandatory tutorial this week: Covers LPWANS, Neighbour discovery
Next two weeks: Optional (NO Attendance)/ Open session
Last week: Sample examination questions discussions/ Open session
Video lectures: Would make sure to record and upload by mid of next week
Notes: ++ We may all have heard of the term Internet of Things. So how are these wireless embedded systems related to the Internet of Things: Today, IoT includes a broad class of devices, including powerful platforms such as smartphones. However, it also includes more resource-constrained devices and what we call Wireless Embedded Systems, and in fact, I consider it to be one of the essential parts of the IoT ecosystem.
++ These are platforms equipped with a radio transceiver, sensor, microcontroller, and some form of energy storage. These platforms also often form a network, and sensor network as it is called has been an active area of research for the past two decades.
++ The research community has also developed wireless embedded platforms which we may know about, and these include: CMUCAM, which is an image sensor platform developed at Carnegie Mellon University, or Permamote is long life sensor platform from the lab I am associated with at UC Berkeley or Lorea which is a long-range backscatter platform that I had developed as part of my doctoral dissertation at Uppsala University. All of these are an example of Wireless Embedded Systems.

## Slide 6
Review of Last Lecture

## Slide 7: Traffic queue sensing and congestion control
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012
[1]
[1]
[1]

## Slide 8: Example application: air quality monitoring
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Purple Air. 2019.
[1]
[2]
[2]

## Slide 9: We need another network option
Requirements:
Wide area of coverage
  Deploy fewer gateways
Low power
  So we can deploy on batteries
Doesn’t need high throughput
  Sensor data is relatively small

## Slide 10: Long-range,low-data needs are not easily met
Bluetooth
WiFi
3G
4G
BLE
Zigbee
Low-Power Wide-Area Networks
2G
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 11: Long-range, Low-power: design choices
How would you design PHY for long-range, low-power ?
  Modulation
    Unclear. Perhaps, not complicated or complex (simple devices)
  Tx Power
    High (much higher than 0 dBm)
  Carrier Frequency Band
    Low (something lower than 2.4 GHz, 915 MHz or lower?)
  Data Throughput
    Low (much lower than 1 Mbps)
  Channel Bandwidth
    Unclear. Likely smaller for lower frequency carrier.

## Slide 12: Design a low-power wide-area network
Any particular MAC choices for lower power?
  Diversity of devices in network
    High power gateway, low power devices in star topology
  Devices should be off whenever possible
    Listen-after send for downlink
  Remove requirements for synchronization
    No TDMA access control if it can be avoided
    Aloha, CSMA

## Slide 13: Long-range CSMA is problematic
Long-range makes everything more challenging
  Kilometers of range mean kilometers between devices
Detection of channel use is less reliable
  Active research in clear channel assessment for LPWANs
Hidden terminal problem has a wider range
  Might make RTS/CTS more important
Result: CSMA doesn’t dominate LPWANs like it does WLANs

## Slide 14: LPWANs overview (common qualities)
Unlicensed 915 MHz band (902-928 MHz)
Higher power transmissions: ~20 dBm (100 mW)
Low data rate 100 kbps or less
Range on the order of multiple kilometers
Simple Aloha access control

## Slide 15: LoRaWAN
Open communication standard built with proprietary LoRa PHY
Operates in the unlicensed band
Low data rate (1-20 kbps) and long range (~5 km)
Most popular LPWAN protocol
  Academic research and industry involvement

## Slide 16: LoRa employs a different modulation scheme
Chirp Spread Spectrum (CSS): Modulation technique where frequency is varied linearly from lowest to highest within a channel

## Slide 17: Chirp Spread Spectrum
Data is modulated in the starting and ending points of chirp
  Frequency increases linearly, modulo bounds of the channel

## Slide 18: Spreading factor of CSS modulation
Spreading Factor is essentially the rate-of-change of frequency
  Slope of the line
  Lower values of spreading factor (steeper slope) are faster data rate
Important: different spreading factors are (mostly) orthogonal!
  Two can overlap in time, space, and channel without a collision

## Slide 19: Channel allocation for LoRa
Sixty-four, 125 kHz uplink channels
  Frequency Hopping over the 64 uplink channels
  Plus eight, 500 kHz overlapping uplink channels (not well used in practice)
Eight, 500 kHz downlink channels

## Slide 20: LoRa data rates
Data Rate Index | Spreading Factor | Bit Rate
125 kHz Uplink Rates |  | 
0 | SF10, 125 kHz | 980 bps
1 | SF9, 125 kHz | 1760 bps
2 | SF8, 125 kHz | 3125 bps
3 | SF7, 125 kHz | 5470 bps
500 kHz Uplink Rates |  | 
4 | SF8, 500 kHz | 12500 bps
500 kHz Downlink Rates |  | 
8 | SF12, 500 kHz | 980 bps
9 | SF11, 500 kHz | 1760 bps
10 | SF10, 500 kHz | 3900 bps
11 | SF9, 500 kHz | 7000 bps
12 | SF8, 500 kHz | 12500 bps
13 | SF7, 500 kHz | 21900 bps
Data rate depend on channel in use, spreading factor
64-channel uplink
  1-5 kbps data rate

## Slide 21: LoRaWAN MAC
Uplink: Aloha - transmit whenever
  Randomly split across 64 uplink channels (reduced odds of collision)
  Devices a different spreading factors also do not collide
  Packets are very long though: up to 400 ms in duration
Downlink: listen-after-send (class A device)
  Two windows for RX on different channels

## Slide 22: LoRa transmissions are received on gateway
No synchronization with the end devices
Instead listen to entire bandwidth simultaneously (12 MHz total)
  Recognize preambles and allocate a hardware to decode packet
    Normal gateways: 8 decoders/ Good gateways: 64 decoders

## Slide 23: LoRa link budget and transmission range
Typical TX power 20 dBm
  Up to 30 dBm for 64-channel hopping
  Up to 26 dBm for 8-channel hopping
Receive sensitivity -119 dBm/-146 dBm (highest SF)
  Compare to -100 dBm for 802.15.4 and -95 dBm for BLE
Resulting range is kilometers in urban environments

## Slide 24: LoRaWAN network providers
Network provides with a deployment of gateways
  The Things Network (predominantly in Europe)
  Helium
    Any can buy and install their own gateway, which serves everyone
    Microtransactions to pay for communication

## Slide 25: Sigfox
Very low-rate (600 bps), very long-range (10+ km) communication
Star-topology networks, with always-listening gateways
  Any number of low-power end devices
Uplink-focused communication
Applications: very low-rate metering

## Slide 26: Sigfox PHY
Unlicensed-band communication
  Europe 868 MHz. US 902-928 MHz (915 MHz band)
Ultra-narrowband 600 Hz (100 Hz Europe) channel bandwidth
  Detection only needs to occur at very specific frequency
  Helps improve signal-to-noise ratio

## Slide 27: Sigfox unbalanced uplink and downlink
Uplink
  600 Hz bandwidth, 600 bps, DBPSK
Downlink
  1.5 kHz bandwidth, 600 bps, GFSK
Particularly optimized for Europe
  Uplink on 1% duty cycle channel, up to 14 dBm
  Downlink on 10% duty cycle channel, up to 27 dBm
Works fine in US too
  Gets more power (24 dBm up is typical, up to 32 dBm down) and more range

## Slide 28: Sigfox link budget
Why transmit at 100-600 bps?
  For greatly increased link budget
Link budget: 150-160 dBm
  Assuming Tx at ~20 dBm
  Means Rx Sensitivity of -130 dBm (10 dBm better than LoRaWAN)
Resulting range: 10-15 km in urban environments
  Except that buildings lead to dead spots in range

## Slide 29: Sigfox MAC
Aloha-style access control (send whenever)
  No acknowledgements!
Send message three times for increased reliability
  Then listen for downlink at a set period later on a known frequency

## Slide 30: Sigfox deployments
Proprietary network with managed deployment
  Like cellular networks
  Sigfox deploys networks and transports data
  140 uplink messages plus 4 downlink message per day
Connectionless communication
  Devices are registered with the networks
  Keys are provided in the software image
  Any deployed Sigfox gateway can collect transmitted data
    Enables mobile applications

## Slide 31: IEEE standard for LPWANs
802.11ah (HaLow) standard in 2016
  First real hardware in 2020
  Still not in real-world use yet
Focus on the indoor-to-outdoor scenario
  Medium range (maximum 1 km)
915 MHz communication
  NOT interoperable with other 802.11 access points and devices
Theoretically up to 356 Mbps
  Practically, most devices are expected to implement 150 kbps to 8 Mbps
n.b.
802 = “area networking”
.3 = “LANs”
.11 = “Wireless LANs”
.15 = “PANs”

## Slide 32: 802.11ah allows multiple bandwidth allocations

## Slide 33: TV whitespaces
Unused TV channels between 54 MHz and 698 MHz
  VHF (54-216 MHz)
  UHF (470-698 MHz)
  6 MHz channel width
Allocated but unused
  FCC allows unlicensed use
  IF you do not interfere with primary users

## Slide 34: Sensing channel use
Variation in use
  Spatial: Cannot assume same channel will be free everywhere
  Temporal: Cannot assume channel will be free at all times
Cognitive radio approach
  Dynamically identify unused portions of spectrum
Database approach
  Let someone else do the scanning. Consult database based on location and time

## Slide 35: Learning Objective for Today’s Lecture
Review: last few lecture’s topics
Bluetooth: Basics
Bluetooth: Advertising
Bluetooth: Connections
Bluetooth: Future
802.15.4: Review
Thread
ZigBee

## Slide 36: Basics of Bluetooth Low Energy (BLE)
Direct device-to-device communication
  Usually: Computer to Thing
  Smartphone to device, Laptop to device, etc.
Focus on making the “Thing” really low energy
  Push energy-intensive requirements onto “Computer”

## Slide 37: BLE Layers
Host – Configuration and Server
  GAP – Generic Access Profile
    Configure advertising
  GATT – Generic Attribute profile
    Configure connections
HCI - Host Controller Interface
Controller - Communication
  Link Layer – send packets
  RF and PHY – send bits
GAP
Host
Controller

## Slide 38: Two different communication modes in BLE
Advertising
  Discovery
  Advertisements – broadcast messages indicating device details
  Ephemeral, uni-directional communication from Advertiser to Scanner(s)
  ALOHA access control
Connections
  Interaction
  Bi-directional communication between Peripheral and Central
  Maintained for some duration
  TDMA access control

## Slide 39: BLE network topology
Advertiser
Peripheral
Advertiser
Advertiser
Peripheral
Central & Scanner
Scanner
Connection
Connection
Advertisement
Advertisement
Advertisement
Advertisement

## Slide 40: Bluetooth devices multiple roles at the same time
Topology picture is a simplification of roles
A single device can have multiple roles simultaneously
  Scanning and Advertising simultaneously
  Peripheral and Scanner and Advertiser simultaneously
  Peripheral and Scanner and Central and Advertiser simultaneously
Also possible:
  One Peripheral can be connected to multiple Central

## Slide 41: BLE frequency
2.4 GHz carrier, Forty 2-MHz channels, 1 Mbps data rate
  37, 38, 39 for advertising
  0-36 for connection (FHSS)

## Slide 42: BLE modulation
Gaussian Frequency-Shift Keying (GFSK)
  Improvement on base Frequency-shift Keying
  Smoother transitions between bits -> reduces nearby interference

## Slide 43: BLE signal strength
What are capabilities of CC2650?

## Slide 44: Packet structure
Same packet structure for both advertisements and connections
  Fields are filled in little endian (the opposite of network byte order )
Access address unique for each connection (randomly chosen)
  In Advertising always set to 0x8E89BED6

## Slide 45: Whitening the data bits
Avoid long series of repetitive bits (all zeros or all ones)
  Would cause RF noise to be more focused in one direction
  Radio hardware desires output to have zero DC-bias (or close to that)
  Great example of the PHY and MAC being interwoven in wireless

## Slide 46: Bit processing pipeline

## Slide 47: Learning Objective for Today’s Lecture
Review: last few lecture’s topics
Bluetooth: Basics
Bluetooth: Advertising
Bluetooth: Connections
802.15.4: Review
Zigbee
Thread

## Slide 48: Advertising
BLE discovery mechanism
  Make nearby devices aware of advertiser’s existence
  Communicate some information from or about advertiser
  Traditional purpose is to enable connections, but this is also useful for general communication
Advertisements
  Periodic broadcast messages with data
Scan Requests/Responses
  Scanner sends responses after getting a request
    Only occurs when scanner is listening

## Slide 49: Advertising packet layering

## Slide 50: BLE advertising header
ADV_IND
  Advertisement
  Allows connections and scan requests
ADV_NONCONN_IND
  Advertisement
  No connections or scan requests
ADV_SCAN_IND
  Advertisement
  No connections but allows scan requests
SCAN_REQ
  Scan request
SCAN_RSP
  Scan response

## Slide 51: Advertisement payloads
AdvA – address of the advertiser
  TxAdd bit from header specifies if this is a “public” or “random” address
Remaining up to 31 bytes are available for use
Putting it all together, up to 47 bytes total:
Preamble 1 Byte | Access Address 4 Bytes | Header 2 Bytes | Advertiser Address 6 Bytes | Advertiser Data (Payload) 0-31 Bytes | CRC 3 Bytes
BLE Packet
Advertising PDU

## Slide 52: Scan Requests and Responses
Scan request
  Just the two addresses: the scanner’s and the advertiser’s
Scan response
  Identical to an advertisement
  But only occurs after a request

## Slide 53: Advertising timing
Advertising Events occur periodically [20ms – 10.24 s] (or longer)
  Plus a random delay after each instance [0-10ms]
  Why?
User picks the rate as a tradeoff of energy and discovery latency

## Slide 54: Advertising timing
Advertising Events occur periodically [20ms – 10.24 s] (or longer)
  Plus a random delay after each instance [0-10ms]
  Why? Collisions
User picks the rate as a tradeoff of energy and discovery latency

## Slide 55: Advertising event
Three transmissions, one on each advertising channel
  Always in the same order
Transmission, followed by listening window on that same channel
  Requests will be sent >=150 us (Inter-Frame Spacing, IFS) after Tx
  Followed by a retune to the next channel frequency
Short listen window to enable low-power operations

## Slide 56: Preserving energy in communication
Most energy is spent listening
  This is due primarily to how long listening durations are compared to transmissions
Example: maximum-sized BLE transmission:
  8 bits/byte * 47 bytes = 376 bits at 1 Mbps = 0.376 ms transmitting
  So listening for an entire second is >2500 times longer
  But listening for only 0.376 ms requires sub-ms synchronization, which itself costs energy to manage…
  Instead, when advertising, nRF radios listen for ~0.200 ms, only after a transmission

## Slide 57: Payload of an advertisement
BLE payload?
  Theoretically whatever you want, but that isn’t very compatible
  Point is to specify capabilities of the advertiser
Desire: specify payloads in such a way that all scanners can interpret what they mean about the device
  This is different from traditional internet packets
  Broadcasts are for _anyone_ to hear, not a specific server/application
Ideas?

## Slide 58: TLV Format
Type – Length – Value
  Actually, BLE does the length part first
  Scanner can hop through length/type pairs to find what interests it

## Slide 59: Payload types
Listed in the Core Specification Supplement [Supplement v9]
  Each might have their own considerations about AD Data format
Flags (supported modes: BLE and Bluetooth) required by Apple?
Name
Service UUID
TX Power Level
Manufacturer-specific data
And about twenty others

## Slide 60: Scanning Pattern
Iterate through channels, listening for advertisements
  Tscan_interval controls rate at which channels are changes
  Tscan_window controls duty cycle of listening
Why listen at a low duty cycle?

## Slide 61: Scanning Pattern
Iterate through channels, listening for advertisements
  Tscan_interval controls rate at which channels are changes
  Tscan_window controls duty cycle of listening
Why listen at a low duty cycle? Save energy

## Slide 62: Putting it all together
Advertisements are received when the channel of the scan window and the channel of the advertisement overlap in time (and space)

## Slide 63: Scanning expectations
Scanners will NOT receive 100% of packets sent
Packets are lost due to one or more of following:
  Duty cycle
  Sharing 2.4 GHz antenna with WiFi
  Retune period after each scanning interval
  Dropped packets in the receive software
  Packet collisions

## Slide 64: Advertisements are already being used for communication
BLE advertisements are uncoordinated, broadcast messages designed for discovery.
Devices are being deployed using advertisements.
  Beacons – iBeacon
  Tracking – Tile
  Local communication – Apple Continuity
Notes: PowerBlade is a great example of this.
  It’s a plug-load power meter
  Initially configured to use advertisements as a simple method for reading measurements with a smartphone
  We are interested in household deployments where dozens of PowerBlades will be deployed to measure all the loads in a home
  Can we still use BLE advertisements for data transfer in the presence of many other devices?

## Slide 65: Beacons
Advertising with advertisements!
Web of Things
  Real-world tags that broadcast virtual-world identifiers
iBeacon and Eddystone
  Formats for sending URLs and device identifiers
  Use existing BLE fields (Service Data and Manufacturer-Specific Data)

## Slide 66: Tracking
Find devices nearby
  Get a sense of distance to the device
Find my X
  Tile: find my keys
  Apple: find my device
Uses TX power level field
  Lists the transmitted power of the device
  Pathloss = TX power – RSSI (all in dBm)

## Slide 67: Problem with RSSI-based distance – not accurate
Pathloss is NOT only due to distance
RSSI is way worse at this than you hope it would be
Citation: literally everyone has made this figure at some point

## Slide 68: Learning Objective for Today’s Lecture
Review: last few lecture’s topics
Bluetooth: Basics
Bluetooth: Advertising
Bluetooth: Connections
Bluetooth: Future
802.15.4: Review
Thread
ZigBee

## Slide 69: Overview of connections
Connections are for bi-directional communication with higher throughput than advertisements
Simple view
  A peripheral is either advertising or in a connection
  A central is scanning and in one or more connections
  (Remember: devices can have many roles simultaneously)
While in a connection both devices act like servers
  Either device can read/write fields available on the other device

## Slide 70: Connection timeline (in picture form)
Central
Peripheral

## Slide 71: Connection timeline
Initiating a connection
  Peripheral is sending broadcast advertisements
  Central is scanning and receives an advertisement
  Central sends connection request
During a connection
  Central sends a packet each “connection interval”
  Peripheral immediately responds with a packet
  Multiple packets may be exchanged this way until done
  Repeat at next connection interval
Ending a connection
  Either device sends termination packet
  Timeout occurs on either device

## Slide 72: Connection request packet
Scanner waits until it sees an advertisement from a device it wants to connect to
  Requesting a connection (in higher layers) just starts this search process
Sends connection request payload in response to advertisement

## Slide 73: Request parameters
Specifies parameters of the connection
  Peripheral must either agree or totally reject the connection
  Peripheral can later propose a change to the connection parameters
Interval is how frequently connection events occur
Timeout is how long since hearing from before the connection breaks
Channel Map and Hop have to do with FHSS pattern

## Slide 74: Data payloads
Length (16 bits) | Channel ID (16 bits) | L2CAP SDU Length* (16 bits) | Information Payload (0 to 249 octets)
SDU – Service Data Unit
Logical packet that may be split into several physical packets
Channel ID
Destination for data
ATTributes or Security
Can also make custom endpoints

## Slide 75: Next steps in a connection
Control packets
  Version
    Bluetooth version, Company ID of Software Stack
  Features
    Various connection features supported by the device
    Encryption, Ping, Channel selection algorithms, Various 5.0 features
  Etc.
    Extended packet length, Various 5.0 features (change PHY)
    Various “procedures” for setting up changes in the connection
Data packets
  Attribute discovery
  Attribute reading

## Slide 76: Ending connections
Termination control packet
Timeout parameter from connection parameters
  Human-based devices may just wander away from each other
  Or be shut off, or reprogrammed, etc.

## Slide 77: Questions about Bluetooth “network”
How does TDMA MAC for connections work?
  Implies a schedule
  Implies synchronization
How many devices can be in a network?
How much throughput can a device have?

## Slide 78: How is the TDMA schedule created/managed?
Only the central needs to know the schedule
  It controls interactions with the peripheral(s) it is connected to
Anchor point and connection interval determines the schedule for a specific device
Central to Peripheral
Central to Peripheral
Peripheral to Central

## Slide 79: How is synchronization managed?
Central sends first packet at each connection interval
  So peripheral must be synchronized to central
  Resynchronization can occur on each received packet
Specification describes how a peripheral must widen its listening window based on “Source Clock Accuracy”

## Slide 80: How many devices can be connected?
We can schedule with granularity of at least 1.25 ms (offset steps)
  That’s at least 800 devices per second
Intervals go up to 4 seconds, so multiply by four
  That’s 3200 devices per max interval
Plus central can skip intervals on occasion without dropping the connection
  And really the offset defines a window. More granularity is available
Answer: thousands of devices
  Although each is sending minimum-sized packets each interval

## Slide 81: How many devices can be connected in the real world?
The limit is much much lower on real devices
  Example: Android sets a limit at around 4-15
  nRF52 s140 softdevice allows up to 20
Connection management is often done in firmware
  Softdevice for nRF, firmware on the radio chip in smartphones
Limited by memory and complexity

## Slide 82: How much throughput can a device have?
1 Mbps?

## Slide 83: How much throughput can a device have?
1 Mbps? Not even close. Packet overhead plus timing delays

## Slide 84: Overview of Generic Attribute Profile (GATT)

## Slide 85: Attribute server keywords
Characteristic
  A field with properties and a value
  Descriptor: metadata about the characteristic
Service
  Collection of characteristics
Profile
  Collection of services

## Slide 86: UUIDs and handles
Universally Unique Identifiers
  128-bit, mostly random with a few bits for versioning
  Example: 00000000-0000-1000-8000-00805F9B34FB
    This is the default BLE UUID for known services
    You can generate your own UUID for custom services
Handles
  Too long to pass around all the time, so pick 16 bits that mean that UUID
    Must be unique among services/characteristics on that device
  Taken from UUID: 0000xxxx-0000-1000-8000-00805F9B34FB
  Handle often sequentially incremented for each new characteristic within a service

## Slide 87: Discovery
When a connection first occurs, each device can query the other for a list of services
  And can further query for a list of characteristics in that service
  Gets a list of handles/UUIDs
Standardized UUIDs can be interpreted immediately
  Custom services/characteristics need documentation from the manufacturer

## Slide 88: Learning Objective for Today’s Lecture
Review: last few lecture’s topics
Bluetooth: Basics
Bluetooth: Advertising
Bluetooth: Connections
Bluetooth: Future
802.15.4: Review
Thread
ZigBee

## Slide 89: Changes in BLE 5
Major changes
  Multiple physical layers
  Advertising extensions
  Localization extensions
Minor changes
  Various quality of life improvements
  Examples:
    Advertise on channels in any order
    Better data channel hopping algorithm

## Slide 90: Revised physical layers
2 Mbps PHY
  Transmit data faster
  Transmit more data in the same time
Coded PHY
  Forward Error Correction in the data stream
    1 bit -> 2 symbols or 8 symbols
  Makes bits more reliable -> longer distance
  500 kbps and 125 kbps modes
Connections can switch to these PHYs after creation
Advertisements can use these with extensions only

## Slide 91: Revised processing path

## Slide 92: Extended advertising
Allow bigger payloads and/or different PHYs
  Uses Data Channels to do so. Why?
  Regular advertisements point to extended advertisements

## Slide 93: Extended advertising
Allow bigger payloads and/or different PHYs
  Uses Data Channels to do so. Why? Packet collisions!
  Regular advertisements point to extended advertisements

## Slide 94: Procedure for scanning extended advertisements
Scan on 3 primary channels for advertising packets.
If ADV_EXT_IND is scanned, record the secondary channel information (which channel and when etc.)
Scan the specific secondary channel at the given time.

## Slide 95: Learning Objective for Today’s Lecture
Review: last few lecture’s topics
Bluetooth: Basics
Bluetooth: Advertising
Bluetooth: Connections
Bluetooth: Future
802.15.4: Review
Thread
ZigBee

## Slide 96: 802.15.4 Overview
Goals
  Explicit support for low-cost, low-power, low-throughput devices
  Focus on low complexity for specification
    Only PHY and MAC are part of specification
  Target home automation
    Secondarily industrial control/monitoring, vehicular sensing, and agricultural uses

## Slide 97: IEEE 802.15.4
Low-Rate Wireless PAN
  250 kbps, ~100 m range
  Radio hardware available with low-power and low-cost
Specification: 2003
  Also 2006, 2011, 2015, and 2020 revisions
    Mostly various added capabilities such as extra PHY layers
    Also define optional security, scheduling, and larger frame sizes
We’ll mostly work off of the 2006 version
  Thread is based on 2006 version
  Zigbee is based on the original 2003 version
  Roughly 200 pages of meaningful specification (100 of appendices)
    Compare to 3000 pages of Bluetooth/BLE

## Slide 98: 802.15.4 RF channels
27 channels across three bands
5 MHz channel separation at 2.4 GHz
  Compare to 2 MHz for BLE

## Slide 99: Regional bands
Different RF bands have different regional availability
Also have different rules
  915 MHz: 400 ms dwell time
  868 MHz: 1% duty cycle

## Slide 100: Learning Objective for Today’s Lecture
Review: last few lecture’s topics
Bluetooth: Basics
Bluetooth: Advertising
Bluetooth: Connections
Bluetooth: Future
802.15.4: Review
Thread
ZigBee

## Slide 101: Thread overview
Build a networking layer on top of 15.4
  Reuses most of PHY and MAC
  Adds IP communication
  Handles addressing and mesh maintenance
Goals
  Simplicity – easy to install and operate
  Efficiency – years of operation on batteries
  Scalability – hundreds of devices in a network
  Security – authenticated and encrypted communication
  Reliability – mesh networking without single point of failure
Industry-focused, but based in academic research

## Slide 102: Changes to Physical Layer
Remove all non-2.4 GHz PHY options
Otherwise the same
  OQPSK
  16 channels, 5 MHz spacing
  Typical TX power 0 dBm
  Typical RX sensitivity -100 dBm

## Slide 103: Changes to Link Layer and MAC
Non-beacon-enabled PAN only
  No superframe structure
  No periodic beacons
  No Guaranteed Time Slots
Throw out most existing MAC Commands
  Remove network joining/leaving
  Remove changing coordinators
  Remove Guaranteed Time Slot request
  Network joining will be handled at a higher layer

## Slide 104: Changes to Link Layer and MAC
Keep unslotted CSMA/CA algorithm
Keep packet structure
Keep Frame Types
  Beacon
  MAC Command
    Beacon Request
    Data Request
  Data
  Acknowledgement

## Slide 105: Combination of star and mesh topology
Routers (parent)
  Mesh communication with other routers
  Radio always on
  Forwards packets for network devices
  Enables other devices to join network
  32 routers per network
End devices (child)
  Communicates with one parent (router)
  Does not forward packets
  Can disable transceiver to save power
    Send packets periodically to avoid timeout
  511 end devices per router

## Slide 106: Router promotion
“Router Eligible End Device”
  A router without any children
  Can operate as an end device with one connection (lower power)
  Promotes to a router when a joining end device relies on it
    If there is room for an additional router (max 32, typical 16-23)

## Slide 107: Other special roles
Thread leader
  Device in charge of making decisions
    Addresses, Joining details
  Automatically selected from routers
    One leader at any given time
    Additional leader is selected if the network partitions
Border router
  Router that also has connectivity to another network
    Commonly WiFi or Ethernet
  Provides external connectivity
  Multiple border routers may exist at once

## Slide 108: Thread uses IPv6 for communication
Why IP?
  If Wireless Sensor Networks represent a future of billions of connected devices distributed throughout the physical world
  Why shouldn’t they run standard protocols wherever possible?
  Why IPv6?
    Generalized, Flexible, Capable
Benefits
  Interoperability with normal computers and networks
  Reuse state of the art developed standards instead of remaking them
    Security, Naming, Discovery, Services
Costs
  Packet overhead can be high (will fix)
  Complexity for supporting protocols
Hui and Culler, “IP is Dead, Long Live IP for Wireless Sensor Networks”. 2008

## Slide 109: Background: IPv6
Replacement to Internet Protocol v4
Extended addressing for devices
  32-bits for IPv4 addresses -> 128-bits for IPv6 addresses
  Example: a39b:239e:ffff:29a2:0021:20f1:aaa2:2112
Supports multiple transmit models
  Broadcast: one-to-all
  Multicast: one-to-many
  Unicast: one-to-one
Various other improvements

## Slide 110: Background: IPv6 address notation rules
Groups of zeros can be replaced with “::”
  Can only use “::” in one place in the address
Leading zeros in a 16-bit group can be omitted
  0000:0000:0000:0000:0000:0000:0000:0001 → ::1
  2345:1001:0023:1003:0000:0000:0000:0000 → 2345:1001:23:1003::
  aecb:0222:0000:0000:0000:0000:0000:0010 → aecb:222::10
Special addresses
  Localhost - ::1 (IPv4 version is 127.0.0.1)
  Link-Local Network - fe80:: (bottom 64-bits are ~device MAC address)
  Local Network – fc00:: and fd00::
  Global Addresses – 2000:: (various methods for allocating bottom bits)

## Slide 111: Background: IPv6 datagram format
Priority: like “type of service” in IPv4.
Flow label: ambiguous
Next header: TCP, UDP
Hop limit = TTL
data
(variable length, typically a TCP or UDP segment)
payload length
next header
hop limit
flow label
priority
version
32 bits
source address
(128 bits)
destination address
(128 bits)
how much overhead?
40 bytes of IPv6
20 more than IPv4

## Slide 112: 6LoWPAN
Method for running IPv6 over 802.15.4 links
  IPv6 over Low-Power Wireless Personal Area Networks
  IETF Standard (RFC4944 + updates in RFC6282)
Directly out of the research world (Jonathan Hui + David Culler)
  Research Paper: IP is Dead, Long Live IP for Wireless Sensor Networks
  Thesis of work: sensor networks can and should use IPv6
Important goals
  Compress IPv6 headers
  Handle fragmentation of packets
  Enable sending packets through mesh

## Slide 113: 6LoWPAN header compression
40 bytes of IPv6 header are a lot for a 127-byte payload
Most important goals
  Communication with devices in the 15.4 network should be low-overhead
  Communication outside of the 15.4 network should still minimize overhead where possible
Assume a bunch of common parameters to save space
  A bunch of options are set to default values
  Payload length can be re-determined from packet length
  Source/Destination addresses can often be reassembled from link layer data
    Plus information about network address assignment known by routers
Border router “inflates” the packet before sending externally

## Slide 114: Example of compression
Note: Thread actually uses IPHC (not HC1) from rfc6282

## Slide 115: 6LoWPAN fragmentation
Only the first packet of the fragments will hold the IPv6 header
  Tag, offset, and size are used to reconstruct

## Slide 116: 6LoWPAN mesh forwarding
Additional header with originator and final addresses
Which of these headers are used depends on the packet

## Slide 117: Benefit to IPv6: multiple address spaces per Thread device
Each device gets an IPv6 address for each way to contact it
  Global IP address
  Mesh-local IP address
  Link-local IP address
  Topology-based IP address
  Role-based IP address(es)

## Slide 118: Traditional addresses in Thread
Link-Local Addresses
  FE80::/16
  Bottommost 64-bits are EUI-64 (MAC address with 0xFFFE in the middle)
  Permanent for a given device (no matter the network)
  Used for low-layer interactions with neighbors (discovery, routing info)
Mesh-Local Addresses
  FD00::/8 (FD00:: and FC00:: are for local networks)
  Remaining bits are randomly chosen as part of joining the network
  Permanent while connection is maintained to a network
  Used for application-layer interactions
Global Addresses
  2000::/3
  Public address for communicating with broader internet through Border Router
  Various methods for allocation (SLAAC, DHCP, Manual)

## Slide 119: Topology-based addresses in Thread
FD00::00ff:fe00:RLOC16
  Same top bits as mesh-local
Routing Locator (RLOC)
  Router ID plus Child ID
Changes with network topology
  Used for routing packets

## Slide 120: Role-based addresses in Thread
Multicast
  FF02::1 – link-local, all listening devices
  FF02::2 – link-local, all routers/router-eligible
  FF03::1 – mesh-local, all listening devices
  FF03::2 – mesh-local, all routers/router-eligible
Anycast
  FD00::00FF:FE00:FCxx
    00 – Thread Leader
    01-0F – DHCPv6 Agent
    30-37 – Commissioner
    etc.

## Slide 121: Open Question
Why use Thread instead of basic 802.15.4?
  Full specification of upper layers
    Clarifies how data is transmitted between devices on a network
    Cleans up a lot of things otherwise left implementation-dependent
  Interaction with the world outside of the sensor network!
    Gateway can be a dumb forwarder of packets
    Devices can directly talk to NTP servers or POST data to a website!

## Slide 122: Discovering Thread networks
Beacon request MAC command
  Routers/Router-eligible devices respond
  Payload contains information about network
Thread network specification
  PAN ID – 16-bit ID
  XPAN ID – extended 64-bit ID
  Network Name – human-readable
Active scanning across channels can quickly find all existing nearby networks

## Slide 123: Creating a new network
Select a channel (possibly by scanning for availability)
Become a router
  Elect yourself as Thread Leader
  Respond to Beacon Requests from other devices
Further organization occurs through Mesh-Level Establishment protocol

## Slide 124: Joining an existing network
All devices join as a child of some existing router
Send a Parent Request (to all routers/router-eligible)
  Using the multicast, link-local address
Receive a Parent Response (from all routers/router-eligible separately)
  Contains information on link quality
Send a Child ID Request (to router with best link)
  Contains parameters about the new child device
Receive a Child ID Response (from that router)
  Contains address configurations

## Slide 125: Becoming a router
Thread tries to maintain 16-23 routers (max 32)
  Goals: path diversity, extend connectivity
Send a Link Request (to all routers/router-eligible)
  Using the multicast, link-local address
Receive Link Accept and Request (from each router separately)
  Forms bi-directional link
Send a Link Accept (to each router individually)

## Slide 126: Communicating with IP
Any communication that layers on top of IP is now possible
  If there is a library to support it
Common choices
  UDP
    DNS – translate hostnames into IP addresses
    SNTP – get real-world time, accuracy better than 1 second
    CoAP – send and receive data

## Slide 127: Constrained Application Protocol - CoAP
HTTP, but over UDP targeting less-capable devices
  Same REST architecture
  Adds capability for automatic retransmissions
CoAP Requests
  Have a type: GET, POST, PUT, DELETE
  Have a URL: /file/etc
  Have data up to 65 KB

## Slide 128: Learning Objective for Today’s Lecture
Review: last few lecture’s topics
Bluetooth: Basics
Bluetooth: Advertising
Bluetooth: Connections
Bluetooth: Future
802.15.4: Review
Thread
ZigBee

## Slide 129: ZigBee goals
Enable automatic communication between devices
  Low complexity
  Low power
  Focus on home automation and industrial control/monitoring
From our perspective
  802.15.4 PHY and MAC
  Designed for higher-power devices than Thread or BLE
    Although still relatively low power

## Slide 130: ZigBee history
Intertwined with the creation of 802.15.4
  Both are founded around the same time
  ZigBee Alliance involved in the original 802.15.4 specification
    Recently renamed: Connectivity Standards Alliance (CSA)
  Original plan: 802.11/WiFi <-> 802.15.4/ZigBee

## Slide 131: ZigBee stack

## Slide 132: Use of 802.15.4
Basic answer: everything
  Reuse all of PHY (including non-2.4 GHz channels)
  Reuse all of MAC (including beacon-enabled network and GTS)
    Same CSMA/CA mechanism

## Slide 133: ZigBee devices (same roles as 802.15.4 defines)
ZigBee Coordinator (ZC)
  Starts the network and decides on key parameters
  Is also a Router
ZigBee Router (ZR)
  Higher-power, more-capable devices
  Radios always on (except during inactive superframe)
  Connect to one or more children
  Connect to one or more routers
ZigBee End Device (ZED)
  Lower-power, less-capable devices
  Always a child of one router

## Slide 134: Older ZigBee - tree networks
Original preferred topology
Uses beacon-enabled network
  Synchronization via beacon superframes
  Can reduce power requirements for routers
Some things get simpler
  Address assignment is simple
    If you restrict network size
  Routing is straightforward
    But likely more hops for router-to-router communication

## Slide 135: ZigBee tree network complications
Distributed routing scheme limits topologies
  There is a limit on number of routers
  Each router has a maximum number of children
  There is a maximum limit for router depth
Needs a beacon scheduling mechanism
  Each parent must both participate in a superframe
  And also send their own superframe beacons
  Need to keep inactive period large if there is significant router depth
  Each beacon includes a TX offset field specifying parent beacon time
    Helps prevent hidden terminal problem

## Slide 136: Modern ZigBee – mesh networks
Presently preferred topology
Uses non-beacon-enabled network
  All routers are always-on devices
  Allows arbitrary communication between routers
Some tradeoffs
  Higher power routers
  Routing more complicated (potentially better algorithms though)
  Addressing more complicated
    Assign random addresses to each node
    Include a method for address conflict resolution

## Slide 137: ZigBee End Device polling
Packets are held in ZigBee Routers for up to 7.68 seconds
  Compare to undefined duration for Thread (at least minutes)
  Reduction in “low energy” capability for end devices
  Limiting timeouts makes Router design simpler
ZigBee codifies polling behavior for End Devices
  Long Polling - steady state polling period, example: 7.5 seconds
  Short Polling – polling period while waiting on data, example: 1 second

## Slide 138: ZigBee application-layer terms
Devices act as servers and clients
Profiles – details application-level features
  Includes network configurations
    For example: security or reliability
  Includes definitions of various Device Types
    Specify a collection mandatory and optional Clusters
    Clusters – collection of Attributes and Commands
      Attributes – information, readable and/or writable
      Commands – control, writable, may elicit a response

## Slide 139: Analogies between BLE and ZigBee
BLE Profile
BLE Service
BLE Characteristic
ZigBee Profile + Device Type
ZigBee Cluster
ZigBee Attribute
Also ~ZigBee Commands

## Slide 140: Example ZigBee network

## Slide 141: A problem: the siloed internet of things
Problem: companies are more interested in selling you the whole stack
  Which then makes it harder for devices to be interoperable
This is not Thread or IP-specific, but a problem all IoT devices are facing

## Slide 142: Matter Wireless Standard

## Slide 143: Wireless Networking
Ambuj Varshney
Assistant Professor, National University of Singapore
Wireless, Embedded Intelligence, Sensing, and Emerging Technologies Group
ambujv@nus.edu.sg