## Slide 1: Wireless Networking
Ambuj Varshney
Assistant Professor, National University of Singapore
Wireless, Embedded Intelligence, Sensing, and Emerging Technologies Group
ambujv@nus.edu.sg

## Slide 2
Administration and Course Logistics

## Slide 3: Assignment 2
Link: https://weiserlab.github.io/ambuj/cs4222_assignment2
Deadline (EXTENDED): 10th of March 2023
Covers: 7% of overall grade
Program Sensor Tag, Implement State Machine, Using Actuators and Sensors
No Plagiarism! We will check for code similarity
  No ChatGPT for this assignment
Submission: We will open link on Canvas
Notes: ++ We may all have heard of the term Internet of Things. So how are these wireless embedded systems related to the Internet of Things: Today, IoT includes a broad class of devices, including powerful platforms such as smartphones. However, it also includes more resource-constrained devices and what we call Wireless Embedded Systems, and in fact, I consider it to be one of the essential parts of the IoT ecosystem.
++ These are platforms equipped with a radio transceiver, sensor, microcontroller, and some form of energy storage. These platforms also often form a network, and sensor network as it is called has been an active area of research for the past two decades.
++ The research community has also developed wireless embedded platforms which we may know about, and these include: CMUCAM, which is an image sensor platform developed at Carnegie Mellon University, or Permamote is long life sensor platform from the lab I am associated with at UC Berkeley or Lorea which is a long-range backscatter platform that I had developed as part of my doctoral dissertation at Uppsala University. All of these are an example of Wireless Embedded Systems.

## Slide 4: Tutorial
This week: Localisation and MAC
Next tutorial: Uploaded tomorrow!
Notes: ++ We may all have heard of the term Internet of Things. So how are these wireless embedded systems related to the Internet of Things: Today, IoT includes a broad class of devices, including powerful platforms such as smartphones. However, it also includes more resource-constrained devices and what we call Wireless Embedded Systems, and in fact, I consider it to be one of the essential parts of the IoT ecosystem.
++ These are platforms equipped with a radio transceiver, sensor, microcontroller, and some form of energy storage. These platforms also often form a network, and sensor network as it is called has been an active area of research for the past two decades.
++ The research community has also developed wireless embedded platforms which we may know about, and these include: CMUCAM, which is an image sensor platform developed at Carnegie Mellon University, or Permamote is long life sensor platform from the lab I am associated with at UC Berkeley or Lorea which is a long-range backscatter platform that I had developed as part of my doctoral dissertation at Uppsala University. All of these are an example of Wireless Embedded Systems.

## Slide 5: Learning Objective for Today’s Lecture
Review: last few lecture’s topics
Basics of Medium Access Control
Classical/Historical Medium Access Control for IoT
Multi-channel MAC
IEEE 802.15.4
WiFi Mac

## Slide 6
Review of Last Lecture

## Slide 7: OSI model of communication layers
Transport
  How to form connections between computers
  TCP and UDP
Network
  How to send packets between networks
  IP
  CS domain: CS340
Data Link
  How to send frames of data
  Ethernet, WiFi
  Our focus
Physical
  How to send individual bits
  Ethernet, WiFi

## Slide 8: Protocols are “layered”
Headers for each layer of communication wrap data
  Data is wrapped with header for the network to make a packet
  Packet is wrapped with header for the link to make a frame
Data
Packet Header
Frame Header
Internet Packet
Ethernet Frame

## Slide 9: Data Link Layer
Framing
  Combine arbitrary bits into a “packet” of data
Logical link control
  Manage transfer between transmitter and receiver
  Error detection and correction
Media access
  Controlling which device gets to transmit next
Inherently coupled to PHY and its decisions

## Slide 10: Framing
Typical packet structure
  Preamble - Existence of packet and synchronization of clocks
  Header - Addresses, Type, Length
  Data - Payload plus higher layer headers (e.g. IP packet)
  Trailer - Padding, CRC
Wireless considerations
  Control information for Physical Layer
  Ensure robustness for header
  Explicit multi-hop routing
  Possibly different data rates for different parts of packet
Preamble | Destination Address | Source Address | Type and Length | Data | CRC

## Slide 11: Error control: detection and recovery
Detection: only detect errors
  Make sure corrupted packets get discarded
  Cyclical Redundancy Checks
    Detect single bit errors
    Detect “burst” errors of several contiguous bits
Recovery: also try to recover from small bit errors
  Forward error correction
  Retransmissions
  Far more important for wireless because the cost of transmission is higher

## Slide 12: Wireless is a shared medium
Wired communication has signals confined to a conductor
  Copper or fiber
  Guides energy to destination
  Protects signal from interference
Wireless communication is inherently broadcast in nature
  Energy is distributed in space
  Signals must compete with other signals in same frequency band

## Slide 13: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”
Eye contact (or raise hand) -> out-of-band communication
Wait until it’s quiet for some time -> carrier sense multiple access
Strict turn order -> time division multiple access
Just speak and hope it works -> ALOHA
Everybody sing at different tones -> frequency division multiple access (stretching the metaphor)

## Slide 14
Review: Taxonomy of multiple-access protocols
Reduce collision,
“manage” retransmission
Avoid collision

## Slide 15: Random access medium access control protocols
No coordination
The simplest: ALOHA
  When a node needs to send, it does so.
  If it hears an acknowledgment within a given duration, transmission is successful
  otherwise, it resends after waiting a random amount of time.
Protocol strength
  minimum overhear
  achieves low delay if the load is light

## Slide 16: ALOHA
ALOHAnet (1971)
  University of Hawaii – Norman Abramson
  First demonstration of wireless packet network
Rules
  If you have data to send, send it
Two (or more) simultaneous transmissions will collide and be lost
  Wait a duration of time for an acknowledgement
  If transmission was lost, try sending again “later”
    Want some kind of exponential backoff scheme here

## Slide 17: Slotted ALOHA
Split time into synchronized “slots”
Any device can transmit whenever it has data
  But it must transmit at the start of a slot
  And its transmission cannot be longer than a slot
  Removes half of the possibilities for collisions!
    At the cost of some synchronization method
time

## Slide 18: ALOHA throughput
It can be shown that traffic maxes out at
  ALOHA: 18.4%
  Slotted ALOHA: 36.8%
Assuming Poisson distribution of transmission attempts
Slotted throughput is double because the “before” collisions can no longer occur

## Slide 19: Carrier Sense Multiple Access
Carrier Sense Multiple Access:
  sense carrier
  If idle,
    send
    wait for ack
    If there isn’t one, assume there was a collision, retransmit
Should we transmit immediately once channel is idle?

## Slide 20: CSMA/CD – CSMA with Collision Detection
Detect collisions during your own transmission
  Works great on wired mediums (Ethernet, I2C)
Somewhere between challenging and impossible for wireless
  Transmit and receive are usually the same antenna
  Receiving while transmitting would be drowned out by transmission
    Remember: TX at 8 dBm and RX at -95 dBm

## Slide 21: Carrier Sense Multiple Access/ Collision Avoidance
CA – Collision Avoidance
if the channel is clear, deferred transmission for a "random" interval
  Choose interval from a uniform distribution with values between 0 and maximum window size Wmax
  reduces the probability of collisions on the channel
How large should Wmax be?
  If interval is long, time is “wasted” …
  If interval is too short?

## Slide 22: Hidden terminal problem
Device A
Device B
Device C

## Slide 23: CSMA with RTS/CTS
Hidden terminal problem means that two transmitters might never be able to detect each other’s transmissions
A partial solution
  When channel is idle, transmitter sends a short Request To Send (RTS)
  Receiver will send a Clear To Send (CTS) to only one node at a time
  RTS collisions are faster and less wasteful than hidden terminal collisions
  Downside: overhead is high for waiting for CTS when contention is low

## Slide 24: Solving Hidden Terminal Problem
A
B
C
RTS
CTS
CTS
OK, I’ll wait …
Should RTS/CTS be used all the time?

## Slide 25
In controlled access, the stations consult one another to find which station has the right to send. A station cannot send unless it has been authorized by other stations.
Review: Taxonomy of multiple-access protocols

## Slide 26
Medium access control: Controlled Access
How do you control who has access to medium?
Reservation
Polling
Token Passing

## Slide 27
Taxonomy of multiple-access protocols
“static” allocation of resources

## Slide 28: FDMA – Frequency Division Multiple Access
Split transmissions in frequency
  Different carrier frequencies are independent
  Fundamentally how RF spectrum is split
Technically, each device uses a separate, fixed frequency
  Walkie-talkies
Conceptually, how RF channels work
  WiFi networks pick different bands
  802.15.4 picks a channel to communicate on

## Slide 29: TDMA – Time Division Multiple Access
Split transmissions in time
  Devices share the same channel
Splits time into fixed-length windows
  Each device is assigned one or more windows
  Can build a priority system here with uneven split among devices
Requires synchronization between devices
  Often devices must listen periodically to resynchronize
  Less efficient use of slots reduce synchronization
    Large guard windows. E.g. 1.5 second slot for a 1 second transmission

## Slide 30: TDMA: Time Division Multiple Access‏
Consider a 1Mbps channel (1,000,000bits/sec)
Divide channel into 1000 (equal) times slots
Each slot is 1ms, and can transmit 1,000 bits
Assign slots to 50 users
  Each user transmits every 50 slots/ms and transmit 20 times/slots per second
  On average, each user can transmit 20kbps
Buffering is needed on both sender and receiver to match the differences in data rates
  sender-side: 20kbps -> 1 Mbps
  Receiver-side: 1Mbps -> 20kbps
Notes: 30
30

## Slide 31: TDMA vs. FDMA
Time
Frequency
In practical systems, TDMA is often combined with FDMA
Frequency
Time
FDMA
Time
Frequency
TDMA
Notes: 31
31

## Slide 32: Orthogonal Frequency Division Multiplexing :OFDM
In FDM, the entire frequency spectrum is dedicated to carry data from a single source
  Example: transmit at 40Mbps over a 20 MHz spectrum
In OFDM, data is divided into many (slower) bit streams and multiple subcarriers (each with smaller spectrum) is used
  Example: divide data source into 40 sources, each 1Mbps

## Slide 33: Spread Spectrum (SS)
Spread-spectrum techniques are methods by which a signal is deliberately spread in the frequency domain, resulting in a signal with a wider bandwidth
Such techniques can be used to establish secure communications, increase resistance to natural interference, jamming and to prevent detection
Concept has been alluded to in 1900s, and applied in some form during WWII

## Slide 34: Spectrum of Combined Signal
Resistant to narrowband interference
Signals are difficult to interpret – appears as if increase in background noise
Can share frequency band with others with minimal interference

## Slide 35: Frequency Hopping (FH)
How does FHSS increase resistance to
  natural interference
  jamming
  detection

## Slide 36: Real-world protocol access control
ALOHA
  BLE advertisements
  Unlicensed LPWANs: Sigfox, LoRaWAN
CSMA
  WiFi (slotted, CSMA/CA)
TDMA
  BLE connections
  Cellular LPWANs: LTE-M and NB-IoT

## Slide 37: Learning Objective for Today’s Lecture
Review: last few lecture’s topics
Basics of Medium Access Control
Classical/Historical Medium Access Control for IoT
Multi-channel MAC
IEEE 802.15.4
WiFi Mac

## Slide 38
Basics of Medium Access Control for Internet of Things

## Slide 39: Medium access control for Internet of Things
For traditional MAC, want
  Low Latency
  High Utilization
  Fair
How about (Internet of Things or energy efficient) MAC?
  Power Consumption is a key consideration.
  (Most) sensor applications have low channel utilization
If energy consumption is the main concern, how would you design the MAC protocol differently?

## Slide 40: Energy consumption of medium access control
The main sources of energy consumption in any contention-based MAC protocol:
  overhearing
  control packet overhead
  data transmission/reception
  idle listening
(1) – (3) occurs only when there is a transmission
(4) occurs even when there is no traffic

## Slide 41: “Life Cycle” of MAC Protocols
(4)
(1) – (3)
(4)
(1) – (3)
(4)
(1) – (3)
Less Traffic
(4)
(1 – (3)
(4)
(1) – (3)
Less Traffic
(4)
(4)

## Slide 42: Idle listening is energy expensive
Idle listening consumes most of the energy as traffic load decreases
Many measurements have shown that idle listening consumes 50–100% of the energy required for receiving
But if you do not listen to the channel, how do detect events/transmissions?

## Slide 43: Duty cycled medium access control protocols
Overhearing or passive listening is very expensive, in particular, if utilization is low
Proposal: Don’t overhear, go to sleep!
Advantage:
  Consume very little energy when radio is idle/inactive
Problem:
  When to wakeup?
Requirements:
  Wakeup schedule must be coordinated
  The “right” nodes must wake up at the “right” time

## Slide 44: Various power saving modes in WiFi

## Slide 45: Various power saving modes in WiFi
Requirements:
  AP is always “on”
  All other nodes within range of AP
OR
  Time synchronization
But what if all nodes are battery powered?

## Slide 46: Let's consider Aloha protocol
Consider the simplest MAC protocol – ALOHA
  No change to the protocol: when a node wants to transmit, it does
Does it work?
  Works when
    There is no contention (usually true when utilization is low)
    The receiver is listening (may not be true with duty cycle)
How to convert ALOHA to work with duty cycle?

## Slide 47: Aloha with Preamble Sampling
Preamble
Data
Sender
Receiver
Sensing
Sensing
Sensing
Sensing
Receiver 1
Sensing
Sensing
ACK
Recv
Receiver 2
Sensing
Sensing
(Possible we can miss the preamble and thus data?)
Sensing

## Slide 48: Aloha with Preamble Sampling
Each receiver periodically (every Tp) wakes up to check if the channel is busy for a duration of (Ts)
  If channel is busy, stays in listening mode until destination of data is known (transmitted), else go back to sleep for a period of (Tp-Ts)
Sender transmits a long preamble (Tp), and then send data packet at the end of the preamble period of packet transmission
Is this protocol energy efficient?
Preamble
Data
Sender
Receiver 1
Sensing
Sensing
ACK
Recv
Sensing
Tp
Ts
TD

## Slide 49: Examples
Parameters:
  TP = preamble length
  TS = preamble sample length
  TD = (data + ack) length
No traffic:
  Duty cycle = TS/TP
Always backlog:
  utilization < (TD) / (TD + TP)

## Slide 50: Example (cont’d)
Very low channel utilization, say x%
1 transmitter and N receivers
Assume transmission and reception energy are the same, so we can only consider {send, receive, listen} duration
When there is transmission
  Transmitter’s energy consumption = (TP+TD)
  Receivers’ energy consumption = N(0.5TP) + TD
When there is no transmission
  All are “receivers”, energy = TS
For very small x, total energy ~ (N+1)TS
  Duty cycle is low if (TS/TP) is low

## Slide 51: Example (cont’d)
Price is latency and maximum utilization
  Latency to send a packet is (TP+TD)
  Maximum utilization is TD/(TP+TD)
Need to balance the conflict among
  Reducing energy consumption
  Providing sufficient throughput
  Lowering end-to-end delay

## Slide 52
Classical/Historical Medium Access Control for Internet of Things

## Slide 53: B-MAC: Medium Access Control
B-MAC is an asynchronous MAC protocol based on preamble sampling. It is one of the earliest medium access control protocol for internet of things
A node turns on its radio periodically to check for activity. If it receives a packet, it stays awake. Otherwise, it goes back to sleep after a timeout
To ensure successful reception, the preamble length must be equal to or much longer than the channel sampling interval
Idle listening occurs when the node samples the channel and finds no activity
For reliable reception, preamble length (Tp) is matched to the interval that the channel is checked for activity
  If the channel is checked every 100ms, preamble must be at least 100ms long
  Idle listening occurs when the node wakes up to sample the channel

## Slide 54: Power Profile of B-MAC

## Slide 55: Improving B-MAC
While the design of B-MAC makes suitable for low power/low duty operations, its performance can be improved
Transmitter:
  Is a long (continuous) preamble necessary?
(Potential) Receivers:
  Is a long (average) waiting period necessary?

## Slide 56: Improving B-MAC with X-MAC
X-MAC improves over B-MAC
  Sender transmits many “probes” with gaps between probes. Each probe contains address of intended receiver
  Receiver checks address embedded in probe, sends acks if it is the destination during the gap period between probes
  Sender transmits DATA, receive replies with Ack to complete data transfer

## Slide 57: ContikiMAC
ContikiMAC is the MAC protocol implemented in Contiki OS

## Slide 58
ts the time to transmit a packet

## Slide 59: Example of timing in Contiki MAC
tr is given by the data sheet of the CC2420 radio transceiver as 0.192 milliseconds.
ti = 0.4 milliseconds
tc = 0.5 milliseconds
Minimum ts = 0.884 milliseconds
  > 0.4 + 2*(0.192)
  Determines the smallest packet size
  With a bitrate of 250kbps, and a 7 byte overhead per packet, minimum packet size using Contiki MAC is 21 bytes

## Slide 60
Receiver wakeup frequency is lower, e.g. 8Hz

## Slide 62: Receiver-Based Preamble Sampling
In B-MAC, X-MAC and Contiki MAC, sender transmits long preamble
Can we switch from sender-initiated to receiver-initiated?
  Is there any advantage?

## Slide 63: Receiver Initiated MAC (RI-MAC)
Change to receiver based (RI-MAC)
  Transmitter wakes up and listens for a period of TP
  Receiver wakeups up every TP and sends a small packet to announce its presence
  Transmitter initiates transmission if the “right” receiver wakes up
Advantage
  Less transmission and hence less collision
  May consume less energy

## Slide 64: Receiver Initiated MAC (RI-MAC)

## Slide 65: Lifetime calculation of B-MAC
Consider a node running B-MAC. It wakes up periodically every 200ms to sample the channel for 2ms. If there is no channel activity, it goes back to sleep. The transmission and reception/listening states draw 10mA
The sleeping state draws 0.1mA. If there is no transmission, what is the average current consumption of a node?
  Average = 0.99 x 0.1 + 0.01 x 10 = 0.099 + 0.1 = 0.199mA
Consider a scenario with sensor node A transmitting a very small packet to node B every 2s and both nodes use B-MAC. Calculate the average current consumption of nodes A and B
Node A: 0.1 (10) + 0.9 * 0.199 = 1 + 0.1791 = 1.1791mA
Node B: 0.1 (5.05) + 0.9 * 0.199 = 0.505 + 0.1791 = 0.6841mA

## Slide 66: Synchronous MAC
Why not let all nodes wakeup at the same time?
SMAC’s solution
  Some form of time division multiplexing
  Divide interval into listening and sleeping
  Percentage of listening period is the “duty cycle”

## Slide 67: Synchronous MAC (SMAC)
Example: 10% duty cycle
  Each node listens for 100ms and sleep for 0.9s
  Each node listens for 1s and sleeps for 9s

## Slide 68: S-MAC

## Slide 69: S-MAC: Challenges
Problem: How to synchronize the schedule of all nodes?
  Initially, nodes are deployed to start after a random time interval
  The node whose timer expires first is the synchronizer
  Boundary nodes adopt multiple schedules

## Slide 70: SMAC Schedule Coordination

## Slide 71: Issue with RTS/CTS (with duty cycle)
Does problem exist if D only sleeps when channel is idle?

## Slide 72
Multi-Channel MAC

## Slide 73: Wireless communication over multiple channels
Why do we need multiple channel for wireless communication?
  Increase throughput
  spatial diversity
  Increase reliability

## Slide 74: Wifi Channels
14 channels designated in the 2.4 GHz range spaced 5 MHz apart (with the exception of a 12 MHz spacing before channel 14)
https://en.wikipedia.org/wiki/List_of_WLAN_channels

## Slide 75: ZigBee Channels

## Slide 76: WiFi Channel Usage

## Slide 77: Cross Channel Interference (CTI)
A. Hithnawi, et.al.,TIIM: Technology-Independent Interference Mitigation for Low-power Wireless Networks, IPSN 2015

## Slide 78: CTI (cont’d)

## Slide 79: Multi Channel MAC Protocols
Use a control channel:
  Use of a default channel and time synchronization for control message exchange
  Nodes switch to a different channel for data communication
All channels are used for data communication:
  Nodes switches to another channel when link quality is bad
  How do we find a “good” channel to switch to?

## Slide 80: TSCH Network
Time is divided into slots, multiple slots form a slotframe
Sends to receiver on slots it is listening on (e.g. green to C, red to A)
Frequency chosen for a timeslot is based on a pseudo-random pattern
Scheduling policy is not standardized

## Slide 81
IEEE 802.15.4: ZigBee

## Slide 82: IEEE 802.15
Wireless Personal-Area Networks (WPAN)
  All the things within the workspace of a person
  Conceptually smaller domain that the Local Area Network
  Realistically about the same thing as a LAN
Formerly included a Bluetooth spec
  Bluetooth SIG took over governance

## Slide 83: 802.15.4 Overview
Goals
  Explicit support for low-cost, low-power, low-throughput devices
  Focus on low complexity for specification
    Only PHY and MAC are part of specification
  Target home automation
    Secondarily industrial control/monitoring, vehicular sensing, and agricultural uses

## Slide 84: IEEE 802.15.4
Low-Rate Wireless PAN
  250 kbps, ~100 m range
  Radio hardware available with low-power and low-cost
Specification: 2003
  Also 2006, 2011, 2015, and 2020 revisions
    Mostly various added capabilities such as extra PHY layers
    Also define optional security, scheduling, and larger frame sizes
We’ll mostly work off of the 2006 version
  Thread is based on 2006 version
  Zigbee is based on the original 2003 version
  Roughly 200 pages of meaningful specification (100 of appendices)
    Compare to 3000 pages of Bluetooth/BLE

## Slide 85: 802.15.4 RF channels
27 channels across three bands
5 MHz channel separation at 2.4 GHz
  Compare to 2 MHz for BLE

## Slide 86: Regional bands
Different RF bands have different regional availability
Also have different rules
  915 MHz: 400 ms dwell time
  868 MHz: 1% duty cycle

## Slide 87: 802.15.4 network topologies
Only specifies PHY and MAC, but has use cases in mind

## Slide 88: Star and Tree topologies
PAN Coordinator
  Receives and relays all messages
  Most capable and power-intensive
Coordinators (a.k.a. Routers)
  Control “clusters”
  Receives and relays to its children
  Communicates up to parent coordinator
End Devices
  Only communicate with single parent coordinator
  Least capable and power intensive

## Slide 89: Mesh networks
Most devices are capable of communicating with multiple neighbors
What are advantages of mesh?
What are disadvantages of mesh?

## Slide 90: Mesh networks
Most devices are capable of communicating with multiple neighbors
What are advantages of mesh?
  Devices can communicate over longer distances
  Device failures less likely to collapse the entire network
What are disadvantages of mesh?
  Some nodes have to spend more energy communicating
  Network protocol becomes more complicated to manage routing

## Slide 91: Modes of operation
Beacon-enabled PAN
  Slotted CSMA/CA
  Structured communication patterns
  Optionally with some TDMA scheduled slots
Non-beacon-enabled PAN
  Unslotted CSMA/CA
  No particular structure for communication
    Could be defined by other specifications, like Thread or Zigbee

## Slide 92: Beacon-enabled superframe structure
Beacons occur periodically [15 ms – 245 seconds]
  Devices must listen to each beacon
Contention Access Period
  Slotted CSMA/CA synchronized by beacon start time
Inactive Period
  No communication occurring. Assumes sleepy devices
Contention Access Period
Beacon
Inactive Period
Beacon
…

## Slide 93: Guaranteed Time Slots (GTS)
PAN Coordinator creates a Contention Free Period with Guaranteed Time Slots
  TDMA schedule assigned to specific devices
  Slots eat up part of the Contention Access Period
  No CSMA/CA within a slot
Contention Access Period
Beacon
Inactive Period
Beacon
Guaranteed Time Slots
…

## Slide 94: Non-beacon-enabled PAN
Same idea, just no beacons
  Which removes synchronization benefit (and slotted CSMA/CA)
  Also removes beacon listening cost
    Devices only need to check for activity before transmitting
  Still need an algorithm to determine when it should receive data
    All the time is a huge energy drain
    Algorithms can get complicated here
    Does BLE mechanism of listen-after-send apply?
      Only if sending to a high-power device, not among equals
Contention Access Period
…

## Slide 95: Receiving messages
Listen during entire contention period
  Can receive direct messages from any other device
  Can immediately respond to messages as well
Request messages from Coordinator
  Make all communication go through Coordinator
  Send a request-for-data packet to coordinator to get information
  Coordinator can include list of devices with pending data in beacon
More complicated listening algorithms are possible

## Slide 96: Clear Channel Assessment (CCA)
The “listen” part of CSMA/CA
Variety of implementations are acceptable
Energy above threshold
  Energy for 8 symbol durations above threshold (RSSI)
Carrier sense
  Valid 802.15.4 carrier signal
Energy AND/OR Carrier

## Slide 97: Slotted CSMA/CA operation
Have data to send
Wait for next backoff slot (synchronized from beacon)
Wait for 0-7 backoff slots (slot is 20 symbol durations: 320 us)
Listen for two empty slots
  Idle: Transmit
  Occupied: wait 0-15 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat (upper limit configurable)
    Next time: 0-31 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat
    Timeout

## Slide 98: Unslotted CSMA/CA operation
Have data to send
Wait for next backoff slot (synchronized from beacon)
Wait for 0-7 backoff slots (slot is 20 symbol durations: 320 us)
Listen for two empty slots
  Idle: Transmit
  Occupied: wait 0-15 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat (upper limit configurable)
    Next time: 0-31 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat
    Timeout

## Slide 99: Base packet format
Synchronization
  Preamble: four bytes of zeros
  Start-of-Packet: 0xA7
PHY Header
  One field: length 0-127
  Why still 8 bits?

## Slide 100: Base packet format
Synchronization
  Preamble: four bytes of zeros
  Start-of-Packet: 0xA7
PHY Header
  One field: length 0-127
  Why still 8 bits? Because computers depend on bytes

## Slide 101: Analysis: maximum goodput
Assume best possible case for data transmission
  122 Bytes per packet
    At 250 kbps -> 3.904 ms
  Plus Inter-frame spacing of 40 symbols
    At 62.5 kBaud -> 0.640 ms
  122 Bytes / 4.544 ms -> 214 kbps
    Compare to BLE advertisements: 9.92 kbps
    Compare to BLE connections: 520 kbps

## Slide 102
WiFi: Medium Access Control and Framing

## Slide 103: Basic WiFi network
Star topology network
Basic Service Set (BSS)
  Access point(s)
  Multiple connected clients
Service Set ID (SSID)
  Identifies network
  Broadcast by access point in beacons

## Slide 104: WiFi superframe structure
Beacon followed by contention-free period followed by contention
  Repeats periodically (default ~100 ms)
  802.15.4 adopted a similar superframe

## Slide 105: WiFi superframe in practice
Continuous contention access period
  Any device may send at any time
  PCF is unused in practice
Periodic beacons
  Which also use CSMA and therefore may be delayed
Time
Delayed Beacon
Beacon
Contention
Based Access

## Slide 106: 802.11 beacons
Transmitted periodically (~100 ms by default)
  Enable discovery of network
    Contain capabilities and SSID for the network (802.11b/g/n/ac)
  Assign contention-free slots if used
  Notify devices of waiting packets
    Traffic Indication Map (TIM) has a bitmap specifying which devices data is for
    Enables devices to sleep, skipping a number of beacons
  Handles broadcast/multicast messages
    Every N beacons includes a notation of available broadcast messages
    Messages are transmitted during next contention access period using normal CSMA
    Defines maximum sleep period for devices (must listen to these beacons)

## Slide 107: Contention-free access
Known as Point Coordination Function (PCF)
  Allocates a contention-free period for specific devices
  Access Point decides when to grant based on requests
Drawbacks
  Latency depends on beacon intervals
  Mechanism for explicit Quality of Service is unclear
PCF is not used in practice

## Slide 108: Contention-based access
Known as Distributed Coordination Function (DCF)
  Base communication method for WiFi (essentially always)
  All packets are immediately ACK’d by receiving device
  Uses CSMA/CA to determine when it can send
    With random backoff
  Problem: packets can be very long (up to 20 milliseconds)
  Solution: Network Allocation Vector (NAV)
    Packets include a notation of their duration
    Sensing the beginning of a packet allows backoff to skip the whole packet duration before continuing

## Slide 109: Reminder: hidden terminal problem
Devices communicating with Access Point may not hear each other
  CSMA fails and Access Point losses both messages
A solution: RTS/CTS (Request/Clear To Send)

## Slide 110: Drawbacks of RTS/CTS
Four packets per data (RTS, CTS, Data, Ack)
  Could have just sent data instead of RTS
Significant portion of traffic are application-layer Acks
  Probably better to just have it fail and try again later
RTS/CTS only used for very large packets in practice
  *It’s mentioned still in 802.11n and 802.11ac, so not entirely unused

## Slide 111: Backoff in WiFi
Listen for activity
  If free
    Wait for Inter Frame Spacing (IFS)
    If still free, transmit
  If busy
    Randomly select a number of backoff Slots
    Count down slots whenever medium is not busy
    If busy when backoff completes:
      Increase maximum backoff Slots
      Repeat
Slot time: basic time unit for protocol
  Total time of: switch from Rx to Tx, plus processing time, plus propagation delay

## Slide 112: Prioritizing packets with varying IFS
Tiered Contention Multiple Access (TCMA)
  Idea: assign different inter-frame spacing based on traffic class
  Inherently prioritizes communication
Acknowledgements sent with Short IFS (SIFS)
  Will always transmit before new data clears CSMA check
New data sent with DCF IFS (DIFS)

## Slide 113: Putting backoff together
Two variables
  Contention Window (CW) – maximum backoff amount
  Backoff Count (BO) – current remaining backoff
When attempting to send, if busy Backoff selected in [0, CW]
  Countdown Backoff slots whenever medium is not busy
  At 0, attempt to transmit if not busy
  If busy, double Window and select Backoff again
802.11g values:
  Slot time= 20 us, CWmin= 15 slots, CWmax= 1023 slots
  SIFS= 10 us, DIFS= 50 us

## Slide 114: 802.11 backoff example
A and B want to send and see the medium is busy
  Followed by an Acknowledgement after SIFS
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B

## Slide 115: 802.11 backoff example
Each chooses a random backoff [0, CW] (we’ll say CW is 32)
  Start counting down backoff slots
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8

## Slide 116: 802.11 backoff example
C wants to send, waits DIFS, and can send immediately
  No other traffic is going on
  A and B pause backoff for packet duration
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8
Arrival C
DIFS
C Traffic

## Slide 117: 802.11 backoff example
A and B used NAV to pause backoff for entire traffic plus ACK
  After DIFS, resume backoff count from its previous value
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8
Arrival C
DIFS
C Traffic
Backoff = 6
Backoff = 4
SIFS
ACK
DIFS

## Slide 118: 802.11 backoff example
B reaches zero backoff, finds channel empty, transmits
  A pauses its backoff again for duration plus ACK
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8
Arrival C
DIFS
C Traffic
Backoff = 6
Backoff = 4
B Traffic
SIFS
ACK
DIFS

## Slide 119: Frame structure for WiFi packets
Frame control (various bits)
  Type of packet (Control, Management, Data)
  Subtype (Association, RTS, CTS, Ack, etc.)
  Indication of to/from “distribution system” (Internet rather than intranet)
Duration
  Specifies on-air time of full packet in microseconds
  Note: no actual length field

## Slide 120
Sequence control
  4-bit fragment number
  12-bit sequence number
Quality of Service control
  Identifies traffic category
High Throughput Control
  Configurations for selecting best data rate
Frame body
  Max size depends on PHY
    ~2000 for lower rates
    ~8000 for 802.11n
    ~11000 for 802.11ac
Frame check sequence
  32-bit CRC

## Slide 121: Sending frames in WiFi
Frame bursting
  Transmit multiple frames in a row
Frame fragmentation
  Split service data over multiple frames
Frame aggregation
  Multiple service data in a single frame
  Allows multiple packets to reach Access Point in a single transmission

## Slide 122: Calculating packet durations
Example duration for a 1500 byte 802.11g packet
  6 Mbps for header
  24 Mbps for payload
  566 μs for total packet
    Plus 44 μs for ACK
https://sarwiki.informatik.hu-berlin.de/Packet_transmission_time_in_802.11

## Slide 123: 802.11e improves MAC layer
Hybrid Coordination Function (HCF)
  Modifies contention-free access (still no one uses it)
  Modifies contention-based access: Enhanced Distributed Channel Access (EDCA)
Modifies Quality of Service based on application
  Example of breaking layering for an optimization
  Categories (lowest to highest priority):
    Background
    Best Effort
    Video
    Voice

## Slide 124: Different priority for different application category
Expand to more IFS lengths for different traffic categories
  Smallest AIFS (equal to DIFS) goes to Voice, Largest to Background
  Contention Window min and max also change for each category
    Selects a probability that most important category goes first

## Slide 125: Multiple queues within a single device

## Slide 126: 802.11e also adds maximum durations
802.11e also defines duration a device can transmit for
  Based on PHY in use and Application category
  Background/Best Effort: one frame per contention win
  Example, up to 11 ms for Voice on 802.11ac
    Could be one really big frame at a low data rate
    Could be multiple frames in a row separated by SIFS

## Slide 127: WiFi capability in microcontrollers
ESP32
  Microcontroller plus WiFi radio in single chip
  (Same idea as nRF52840)
Capabilities
  802.11b/g/n 2.4 GHz only
  20 MHz or 40 MHz channels
  Single antenna only (no MIMO)
  MCS0-7
    7 Mbps – 150 Mbps
  Tx power up to 20.5 dBm

## Slide 128: Low power WiFi
Question: should a microcontroller stay connected or reconnect?
  Light sleep: stay connected always, only listening to beacons
  Deep sleep: reconnect to network each time data is ready
Answer for ESP32 depends on security and data interval
  Resecuring during connection takes lots of energy
    Crossover point is about 60 seconds
  Insecure transmissions have a crossover of 5-15 seconds
https://blog.voneicken.com/2018/lp-wifi-esp-comparison/#conclusions

## Slide 129: 802.11ax (2021)
Standard approved on February 9th 2021
  First devices started supporting it in 2019 (WiFi 6)
6 GHz band (WiFi 6E)
  1.2 GHz of bandwidth (5.925-7.125 GHz)
  2020: US FCC made band available for unlicensed use!!!
  EU is expected to follow in March 2021
OFDMA
  MAC scheduling variant of OFDM
  Schedule devices based on time and subcarrier allocations

## Slide 130: 6 GHz band is an enormous amount of bandwidth

## Slide 131: Orthogonal Frequency Division Multiple Access
OFDM: split channel into subcarriers and transmit on those
OFDMA: allocate subcarriers to a device for an amount of time
  Turns OFDM into an access control mechanism
  Complicated question: which device gets which subcarriers at which time?

## Slide 132: Learning Objective for Today’s Lecture
Review: last few lecture’s topics
Basics of Medium Access Control
Classical/Historical Medium Access Control for IoT
Multi-channel MAC
IEEE 802.15.4
WiFi Mac

## Slide 133: Wireless Networking
Ambuj Varshney
Assistant Professor, National University of Singapore
Wireless, Embedded Intelligence, Sensing, and Emerging Technologies Group
ambujv@nus.edu.sg