## Slide 1: Wireless Networking
Ambuj Varshney
Assistant Professor, National University of Singapore
Wireless, Embedded Intelligence, Sensing, and Emerging Technologies Group
ambujv@nus.edu.sg

## Slide 2
Administration and Course Logistics

## Slide 3: Assignment 3a
Link: https://weiserlab.github.io/ambuj/cs4222_assignment3a
Deadline :31st of March 2023
Covers: 13% of overall grade
Wireless measurements using RSSI
No Plagiarism! We will check for code similarity
  No ChatGPT for this assignment
Submission: We will open link on Canvas
Notes: ++ We may all have heard of the term Internet of Things. So how are these wireless embedded systems related to the Internet of Things: Today, IoT includes a broad class of devices, including powerful platforms such as smartphones. However, it also includes more resource-constrained devices and what we call Wireless Embedded Systems, and in fact, I consider it to be one of the essential parts of the IoT ecosystem.
++ These are platforms equipped with a radio transceiver, sensor, microcontroller, and some form of energy storage. These platforms also often form a network, and sensor network as it is called has been an active area of research for the past two decades.
++ The research community has also developed wireless embedded platforms which we may know about, and these include: CMUCAM, which is an image sensor platform developed at Carnegie Mellon University, or Permamote is long life sensor platform from the lab I am associated with at UC Berkeley or Lorea which is a long-range backscatter platform that I had developed as part of my doctoral dissertation at Uppsala University. All of these are an example of Wireless Embedded Systems.

## Slide 4: Assignment 3b and Tutorial
To be announced this week. Deadline: 31st of March 2023
Tutorial this week: Medium Access Control
Notes: ++ We may all have heard of the term Internet of Things. So how are these wireless embedded systems related to the Internet of Things: Today, IoT includes a broad class of devices, including powerful platforms such as smartphones. However, it also includes more resource-constrained devices and what we call Wireless Embedded Systems, and in fact, I consider it to be one of the essential parts of the IoT ecosystem.
++ These are platforms equipped with a radio transceiver, sensor, microcontroller, and some form of energy storage. These platforms also often form a network, and sensor network as it is called has been an active area of research for the past two decades.
++ The research community has also developed wireless embedded platforms which we may know about, and these include: CMUCAM, which is an image sensor platform developed at Carnegie Mellon University, or Permamote is long life sensor platform from the lab I am associated with at UC Berkeley or Lorea which is a long-range backscatter platform that I had developed as part of my doctoral dissertation at Uppsala University. All of these are an example of Wireless Embedded Systems.

## Slide 5
Review of Last Lecture

## Slide 6: B-MAC: Medium Access Control
B-MAC is an asynchronous MAC protocol based on preamble sampling. It is one of the earliest medium access control protocol for internet of things
A node turns on its radio periodically to check for activity. If it receives a packet, it stays awake. Otherwise, it goes back to sleep after a timeout
To ensure successful reception, the preamble length must be equal to or much longer than the channel sampling interval
Idle listening occurs when the node samples the channel and finds no activity
For reliable reception, preamble length (Tp) is matched to the interval that the channel is checked for activity
  If the channel is checked every 100ms, preamble must be at least 100ms long
  Idle listening occurs when the node wakes up to sample the channel

## Slide 7: Improving B-MAC with X-MAC
X-MAC improves over B-MAC
  Sender transmits many “probes” with gaps between probes. Each probe contains address of intended receiver
  Receiver checks address embedded in probe, sends acks if it is the destination during the gap period between probes
  Sender transmits DATA, receive replies with Ack to complete data transfer

## Slide 8: ContikiMAC
ContikiMAC is the MAC protocol implemented in Contiki OS

## Slide 9: Receiver Initiated MAC (RI-MAC)
Change to receiver based (RI-MAC)
  Transmitter wakes up and listens for a period of TP
  Receiver wakeups up every TP and sends a small packet to announce its presence
  Transmitter initiates transmission if the “right” receiver wakes up
Advantage
  Less transmission and hence less collision
  May consume less energy

## Slide 10: Receiver Initiated MAC (RI-MAC)

## Slide 11: WiFi Channel Usage

## Slide 12: Cross Channel Interference (CTI)
A. Hithnawi, et.al.,TIIM: Technology-Independent Interference Mitigation for Low-power Wireless Networks, IPSN 2015

## Slide 13: Cross Technology Interference

## Slide 14: Multi Channel MAC Protocols
Use a control channel:
  Use of a default channel and time synchronization for control message exchange
  Nodes switch to a different channel for data communication
All channels are used for data communication:
  Nodes switches to another channel when link quality is bad
  How do we find a “good” channel to switch to?
Why do we need multiple channel for wireless communication?
  Increase throughput
  spatial diversity
  Increase reliability

## Slide 15: TSCH Network
Time is divided into slots, multiple slots form a slotframe
Sends to receiver on slots it is listening on (e.g. green to C, red to A)
Frequency chosen for a timeslot is based on a pseudo-random pattern
Scheduling policy is not standardized

## Slide 16: 802.15.4 Overview
Goals
  Explicit support for low-cost, low-power, low-throughput devices
  Focus on low complexity for specification
    Only PHY and MAC are part of specification
  Target home automation
    Secondarily industrial control/monitoring, vehicular sensing, and agricultural uses

## Slide 17: 802.15.4 RF channels
27 channels across three bands
5 MHz channel separation at 2.4 GHz
  Compare to 2 MHz for BLE

## Slide 18: 802.15.4 network topologies
Only specifies PHY and MAC, but has use cases in mind

## Slide 19: Star and Tree topologies
PAN Coordinator
  Receives and relays all messages
  Most capable and power-intensive
Coordinators (a.k.a. Routers)
  Control “clusters”
  Receives and relays to its children
  Communicates up to parent coordinator
End Devices
  Only communicate with single parent coordinator
  Least capable and power intensive

## Slide 20: Mesh networks
Most devices are capable of communicating with multiple neighbors
What are advantages of mesh?
  Devices can communicate over longer distances
  Device failures less likely to collapse the entire network
What are disadvantages of mesh?
  Some nodes have to spend more energy communicating
  Network protocol becomes more complicated to manage routing

## Slide 21: Modes of operation
Beacon-enabled PAN
  Slotted CSMA/CA
  Structured communication patterns
  Optionally with some TDMA scheduled slots
Non-beacon-enabled PAN
  Unslotted CSMA/CA
  No particular structure for communication
    Could be defined by other specifications, like Thread or Zigbee

## Slide 22: Beacon-enabled superframe structure
Beacons occur periodically [15 ms – 245 seconds]
  Devices must listen to each beacon
Contention Access Period
  Slotted CSMA/CA synchronized by beacon start time
Inactive Period
  No communication occurring. Assumes sleepy devices
Contention Access Period
Beacon
Inactive Period
Beacon
…

## Slide 23: Guaranteed Time Slots (GTS)
PAN Coordinator creates a Contention Free Period with Guaranteed Time Slots
  TDMA schedule assigned to specific devices
  Slots eat up part of the Contention Access Period
  No CSMA/CA within a slot
Contention Access Period
Beacon
Inactive Period
Beacon
Guaranteed Time Slots
…

## Slide 24: Non-beacon-enabled PAN
Same idea, just no beacons
  Which removes synchronization benefit (and slotted CSMA/CA)
  Also removes beacon listening cost
    Devices only need to check for activity before transmitting
  Still need an algorithm to determine when it should receive data
    All the time is a huge energy drain
    Algorithms can get complicated here
    Does BLE mechanism of listen-after-send apply?
      Only if sending to a high-power device, not among equals
Contention Access Period
…

## Slide 25: Clear Channel Assessment (CCA)
The “listen” part of CSMA/CA
Variety of implementations are acceptable
Energy above threshold
  Energy for 8 symbol durations above threshold (RSSI)
Carrier sense
  Valid 802.15.4 carrier signal
Energy AND/OR Carrier

## Slide 26: Basic WiFi network
Star topology network
Basic Service Set (BSS)
  Access point(s)
  Multiple connected clients
Service Set ID (SSID)
  Identifies network
  Broadcast by access point in beacons

## Slide 27: WiFi superframe structure
Beacon followed by contention-free period followed by contention
  Repeats periodically (default ~100 ms)
  802.15.4 adopted a similar superframe

## Slide 28: WiFi superframe in practice
Continuous contention access period
  Any device may send at any time
  PCF is unused in practice
Periodic beacons
  Which also use CSMA and therefore may be delayed
Time
Delayed Beacon
Beacon
Contention
Based Access

## Slide 29: Contention-based access
Known as Distributed Coordination Function (DCF)
  Base communication method for WiFi (essentially always)
  All packets are immediately ACK’d by receiving device
  Uses CSMA/CA to determine when it can send
    With random backoff
  Problem: packets can be very long (up to 20 milliseconds)
  Solution: Network Allocation Vector (NAV)
    Packets include a notation of their duration
    Sensing the beginning of a packet allows backoff to skip the whole packet duration before continuing

## Slide 30: Backoff in WiFi
Listen for activity
  If free
    Wait for Inter Frame Spacing (IFS)
    If still free, transmit
  If busy
    Randomly select a number of backoff Slots
    Count down slots whenever medium is not busy
    If busy when backoff completes:
      Increase maximum backoff Slots
      Repeat
Slot time: basic time unit for protocol
  Total time of: switch from Rx to Tx, plus processing time, plus propagation delay

## Slide 31: Prioritizing packets with varying IFS
Tiered Contention Multiple Access (TCMA)
  Idea: assign different inter-frame spacing based on traffic class
  Inherently prioritizes communication
Acknowledgements sent with Short IFS (SIFS)
  Will always transmit before new data clears CSMA check
New data sent with DCF IFS (DIFS)

## Slide 32: Putting backoff together
Two variables
  Contention Window (CW) – maximum backoff amount
  Backoff Count (BO) – current remaining backoff
When attempting to send, if busy Backoff selected in [0, CW]
  Countdown Backoff slots whenever medium is not busy
  At 0, attempt to transmit if not busy
  If busy, double Window and select Backoff again
802.11g values:
  Slot time= 20 us, CWmin= 15 slots, CWmax= 1023 slots
  SIFS= 10 us, DIFS= 50 us

## Slide 33: 802.11 backoff example
A and B want to send and see the medium is busy
  Followed by an Acknowledgement after SIFS
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B

## Slide 34: 802.11 backoff example
Each chooses a random backoff [0, CW] (we’ll say CW is 32)
  Start counting down backoff slots
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8

## Slide 35: 802.11 backoff example
C wants to send, waits DIFS, and can send immediately
  No other traffic is going on
  A and B pause backoff for packet duration
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8
Arrival C
DIFS
C Traffic

## Slide 36: 802.11 backoff example
A and B used NAV to pause backoff for entire traffic plus ACK
  After DIFS, resume backoff count from its previous value
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8
Arrival C
DIFS
C Traffic
Backoff = 6
Backoff = 4
SIFS
ACK
DIFS

## Slide 37: 802.11 backoff example
B reaches zero backoff, finds channel empty, transmits
  A pauses its backoff again for duration plus ACK
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8
Arrival C
DIFS
C Traffic
Backoff = 6
Backoff = 4
B Traffic
SIFS
ACK
DIFS

## Slide 38: Learning Objective for Today’s Lecture
Review: last few lecture’s topics
Node Discovery
Routing
IoT/Sensor Network Routing
Flooding
RPL
Misc and Case Study

## Slide 39
Node Discovery

## Slide 40: How to discover nodes or devices nearby
Scenarios for local discovery
  You just enter a shopping mall. You would like to check if there is WiFi service. How does your mobile phone discover the presence of WiFi networks?
  Small sensor devices with only low power network interface (e.g. ZigBee) are deployed in the surrounding and carried by humans. How can these devices discover other devices in communication range (in an energy efficient way)?

## Slide 41: How to perform local neighbor discovery?
Problem is “easy” to solve if there is no constraint and all nodes can be active all the time.
  Challenge is to design a protocol that is energy efficient.
Two broad methods for local neighbor discovery:
  Synchronous
  Asynchronous

## Slide 42: Synchronous neighbor discovery
All nodes are synchronized to the same clock/time.
Nodes wakeup periodically at same time to transmit/receive packets
Node A discovers node B when it hears a transmission from node B
Example:
  Assume time is divided into slots of 100ms and there is a global starting reference time t0 sec
  With a 10% duty cycle, period is 1s,
    each node wakes up at t0 + k sec for 100ms, where k = 0,1,2,3,4….
  With a 1% duty cycle, period is 10s,
    each node wakes up every t0 + 10k sec for 100ms, where k = 0,1,2,3,4….

## Slide 43: What are the drawbacks to synchronous neighbour discovery?
Synchronization can be expensive and periodically re-synchronization will be needed to correct for clock drift over time
As all nodes wakeup at the same time to transmit/receive, collision may increase if too many node transmit simultaneously

## Slide 44: Synchronous neighbor discovery with Asymmetric Nodes
Some nodes are more powerful and is always “ON”
Example: WiFi APs (always ON) vs. mobile device (stays in OFF state as much as possible)
A mobile device wants to discover nearby APs
  APs are always awake
  Mobile device broadcasts (how often?) a probe beacon and listens for replies
    How about AP periodically broadcasts and mobile replies?
A mobile device is associated with an AP but wants to conserve energy by going into sleep state whenever there is no data communication
  How does the device know there is data from the AP if it is in sleep state?

## Slide 45: Power Save Mode (Infrastructure)
When a mobile device wants to go into Power Save Mode (PSM), it informs the AP and goes into sleep state (switches off its radio)
Any packets arriving at the AP for the mobile device in PSM are stored in the AP’s buffer
The AP sends a beacon frame after every fixed time interval. The beacon frame has a field called traffic indication map (TIM) to inform the device in PSM about incoming packets.
Device in PSM wakes up periodically to listen to beacon frames and switch to active state if there are incoming packets

## Slide 46: Power Save Mode (Infrastructure)
TIM – beacon interval for unicast packets
DTIM – beacon interval for broadcast packets
AP
Device 1
Device 2

## Slide 47: Asynchronous Protocols
Challenges:
  No time synchronization
  All nodes are resource constrained
Assumptions
  Divide into time slots (e.g. 100ms)
  Each device decides (randomly?) which time slots to wakeup to transmit/listen
How long will two such devices take to discover each other?

## Slide 48: Birthday Paradox
In a group of N people, what is the probability that there is at least one pair of people who have the same birthday? (assume 365 days in a year)
In general, Prob = 1 – P(none of the N people have the same birthday)
  N = 2, Prob = 1 – (364/365)
  N = 3, Prob = 1 – (364/365)(363/365)
  N = 4, Prob = 1 – ((364/365)(363/365)(362/365)
  N = n, Prob = 1 – 365!/(365n(365-n)!)
Example:
  N = 2, Prob = 0.0027
  N = 23, Prob = 0.5073
  N = 50, Prob = 0.9704

## Slide 49
“Birthday” Protocol
Easy to implement
Good average discovery latency but unbounded worst case
Notes: Next, we will have a brief literature review for neighbor discovery protocols.
Basically, the neighbor discovery solutions can be classified into two types: the asynchronous protocols and synchronized protocols.
Here is the representative work on asynchronous protocols. Nodes use local clock to schedule wireless interface wake-sleep for neighbor discovery purpose.
Asynchronous protocols are the state of the art… The latest research was searchLight in 2012.
key limitation is not scalable to low duty cycle.

## Slide 50: Application to Asynchronous Discovery Michael J McGlynn and Steven A Borbash. Birthday protocols for low energy deployment and flexible neighbor discovery in ad hoc wireless networks. In MobiHoc, 2001
Two nodes randomly choose to wakeup k time slots out of a total n slots. What is the probability that they wakeup at the same time slot at least once?
Probability (Q) can be written down as:
(1%) n = 100, k = 1, Q(100,1) = 0.01
(5%) n = 100, k = 5, Q(100,5) = 0.23
(1%) n = 1000, k = 10, Q(1000,10) = 0.096
(5%) n = 1000, k = 50, Q(1000, 50) = 0.928
Drawbacks – probabilistic bound for discovery time, can take very long sometimes
Can we do better in terms of the worst case?

## Slide 51: Asynchronous – Deterministic Bound Yu-Chee Tseng, Chih-Shun Hsu, and Ten-Yueng Hsieh. Power-saving protocols for IEEE 802.11-based multi-hop ad hoc networks. In INFOCOM, 2002.
Period is n2 slots, active slots = 2n – 1; Duty cycle = (2n-1)/ n2
n = 4, period = 16 slots, duty cycle = 43.75%
n = 10, period = 100 slots, duty cycle = 19%
n = 100, period = 10,000 slots, duty cycle ~ 2%

## Slide 52: Asynchronous – Different Starting Slot
Starting point shifts by N slots
  time slots change from i to (i+N) mod 16
Let N=2 (shift schedule of right table to the reference of the left table)
  {2,6,8,9,10,11,14} becomes {4,8,10,11,12,13,0}
0 | 1 | 2 | 3
4 | 5 | 6 | 7
8 | 9 | 10 | 11
12 | 13 | 14 | 15
0 | 1 | 2 | 3
4 | 5 | 6 | 7
8 | 9 | 10 | 11
12 | 13 | 14 | 15

## Slide 53: Some Limitations
Nodes choose same duty cycle
Duty cycle ~ 1/n
Worst case latency ~ n^2

## Slide 54: DISCO[1] – Another Asynchronous Algorithm
Scheduling radio wake times at multiples of prime numbers to ensure deterministic discovery
  Nodes can have different duty cycles
Version 0: A node i picks a prime number, say pi and wakes up pi timeslots, the duty cycle is (1/ pi). In the worst case, two nodes pi and pj will meet after (pi * pj) timeslots.
  Problem: what if both nodes pick the same prime number?
Version 1: A nodes i picks a prime number, say pi1 and pi2 (pi1 != pi2), wakes up every pi1 and pi2 timeslots. The duty cycle is (1/pi1 + 1/pi2)
  If both nodes pick the same pair of prime number:
    Duty cycle ~ (pi1 + pi2)/ pi1 pi2, Worst Case ~ pi1 pi2
[1] Dutta, Prabal, and David Culler. "Practical asynchronous neighbor discovery and rendezvous for mobile sensing applications." Proceedings of the 6th ACM conference on Embedded network sensor systems. 2008.

## Slide 55: Asynchronous Protocols [1]
Category |  | Representative Protocols | Delay Bound
Asynchronous protocols | Asynchronous probabilistic | Birthday Protocol [2001] | None
 | Asynchronous deterministic | Quorum-based [2002,2005], Disco [2008], U-connect [2010], SearchLight [2012] | 
f is the duty cycle (e.g. 1%)
T is the time slot length (e.g. 20ms)
[1] Xiangfa Guo, Binbin Chen and Mun Choon Chan, "Analysis and Design of Low-Duty Protocol for Smartphone Neighbor Discovery," IEEE Transactions on Mobile Computing, Dec 2017.
Notes: Next, we will have a brief literature review for neighbor discovery protocols.
Basically, the neighbor discovery solutions can be classified into two types: the asynchronous protocols and synchronized protocols.
Here is the representative work on asynchronous protocols. Nodes use local clock to schedule wireless interface wake-sleep for neighbor discovery purpose.
Asynchronous protocols are the state of the art… The latest research was searchLight in 2012.
key limitation is not scalable to low duty cycle.

## Slide 56
Routing

## Slide 57: Routing goals
Have a packet, have a destination, how do we connect them?
Simple techniques
  Broadcast, tree structures
Mesh techniques
  Understand the available routes and select a “good” one

## Slide 58: Performing routing in the wired networks
Routing is trivial if all nodes are connected to each other
Problem: if they are N nodes, need N(N-1) or O(N2) (uni-directional) links

## Slide 59: Performing routing in the wired networks
Number of links can be reduced significantly with one “BIG” switch with N links and routing is still simple
Problem: If N is large and nodes can be far apart (think of the Internet)
Adding more switches/routers reduces the size of the switches/routers needed and allow network to grow
But Routing will be more complex!

## Slide 60: Performing routing in the wireless networks
Routing protocols are complex, hard to maintain/debug and incurred significant overhead. More so for wireless networks.
In practice, wireless network deployments are single-hop and routing is trivial. All stations/devices communicating directly with base stations
  Example: WiFi, Cellular Network, LoRa
  Can one-hop communication be always sufficient by using sufficiently long range radio and large number of base stations?
Why multi-hop routing?
  is strictly better in terms of reach/coverage for the same number of base stations
  provides more routes, potentially more robust

## Slide 61: For the same distance, is it better to have direct or multi-hop path?
A
B
A
D
C
B
E
Which option is better?
Typically, a single-hop is considered better

## Slide 62: But, for energy Consumption …
Is multiple-hop transmission more energy efficient than a single-hop ?
Let us Recall the free space model: Pr = C Pt / da (C = constant)
Transmission over a distance d, let minimum received power needed be P0
  1 transmission to cover distance d, transmission power (P1) needed is
    P0 = C P1 / da or P1 = P0/C * da
  N transmissions to cover distance d, transmission power needed (PN) per hop is
    P0 = C PN / (d/N)a , or PN = P0 /C * (d/N)a
    Total transmission power is N PN = N P0 /C * (d/N)a
Which approach (1 transmission vs N transmissions) is more energy efficient?

## Slide 63: Simple routing solutions
Broadcast
  The link-layer solution for everything
Star topology
  Only one location to send to: parent
  Single parent needs to store information about all children
    Addresses, schedules, etc.
Tree topology
  Two choices: send to descendent or send to parent
  Each parent needs to store information about all children beneath it
  Original ZigBee approach (knowledge built into addressing scheme)

## Slide 64: Many-to-one routing
Tree optimization for sensor networks
  Keep all devices except the “gateway” as simple as possible
Each device only needs to remember hop to gateway
  If gateway wants to send message back, it must include a full hop path

## Slide 65: Communicating using wireless mesh
Formed by a network of static wireless nodes
Issues:
  Interference
  Self-Interference
Selects routes that minimize
  Interference
  Error

## Slide 66: Mesh Routing
Mesh topology makes routing question more complicated
  Multiple hops in a route
  Multiple routes between source and destination
  Becomes a graph theory question based on cost metric
A
B
C
D
E
F

## Slide 67: Flooding
Mesh equivalent of broadcast
  Each node sends to each other node
  Eventually packets will reach the desired destination
  Not really routing at all…
Question: how do we make it stop?

## Slide 68: Flooding
Mesh equivalent of broadcast
  Each node sends to each other node
  Eventually packets will reach the desired destination
  Not really routing at all…
Question: how do we make it stop?
  Maximum retransmissions counter on each packet
    Decrement at each hop. Drop packet when it hits zero
    Need some guess for how many hops to destination
  Keep some history of recently flooded packets
    Don’t retransmit a recently sent packet

## Slide 69: Reactive routing
Build up a map of the routes through a network
  Hopefully the “optimal” routes
Map routes in reaction to a packet arrival
  Sensor devices are slow and limited
  Most likely to resend to same prior address
  Discover a route when it is needed, then cache for next time

## Slide 70: Ad-hoc On-demand Distance Vector Routing (AODV)
On-demand: Construct routes only when needed
Modern ZigBee routing approach (for Mesh topology)
Routing table
  Destination node -> Next hop (for all cached destinations)
  Store only next hop instead of full route
    All routers along the path must also have Destination->Next mappings
  Also keep hops-to-destination and last-seen-destination-sequence-number
Route discovery
  Upon demand: check table
  If not cached send Route Request (RREQ) via Flooding
    Route is unknown, so flooding is needed

## Slide 71: AODV Route Requests (RREQs)
Request ID identifies this RREQ
  Used to discard duplicates during flooding
Sequence Numbers are per-device, monotonically increasing
  Used as a notion of “how recently” device has been seen
  Source SeqNo is the source’s most recent sequence number
  Destination SeqNo is the most recently seen from the destination by the source. (Defaults to zero)
Hop Count is the number of hops this request has taken
  Starts at 1 and incremented by each transmitter along the path
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count

## Slide 72: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
A wants to find a route to F, so it sends out an RREQ

## Slide 73: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 1
B and D also opportunistically add a routing table entry for A

## Slide 74: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 2
B goes first via some access control protocol (D also in contention)
A and D ignore duplicate Request ID C opportunistically adds a routing table entry to A

## Slide 75: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 2
D goes next by some access control protocol (C also in contention)
A, B, and C ignore duplicate Request ID E and F opportunistically adds a routing table entry to A

## Slide 76: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 3
C and E repeat this process with Hop Count 3 (but everyone ignores them)
They go one-at-a-time, but I’m getting tired of drawing these
Actually, they’re in contention with the response from F

## Slide 77: AODV Route Response (RREP)
Reply is sent unicast back to the source via newly constructed route
  Each node along the way already knows the route back
Includes most recent destination sequence number as a sense of recency
  No need for source sequence number anymore
Source Address | Destination Address | Destination SeqNo | Hop Count

## Slide 78: Example AODV RREP (F to A)
A
B
C
D
E
F
Source Address | Destination Address | Destination SeqNo | Hop Count
F | A | 7 | 2
F sends response back to A via D
D opportunistically adds a routing table entry for F

## Slide 79: RREP optimization
An intermediate node responds with RREP if it has a path to destination with a more recent Destination sequence number
  Source may get multiple RREP responses with different recency and hop counts
Note: we’re optimizing for some combination of most recent and lowest hop count

## Slide 80: Route maintenance in AODV
If a link in the routing table breaks, all active neighbors are informed with Route Error (RERR) messages
  After some number of retransmissions and timeouts
  RERR contains destination address that broke
Nodes receiving RERR can start RERQ for destination address
  Which lets them find a new path through the network
  And updates everyone’s cached next-hops

## Slide 81: Dynamic Source Routing (DSR)
Another reactive routing technique
  Similar design as AODV
In DSR, routing tables have full route to destination
  Each packet transmission includes a list of hops to destination
  So the route to an important destination only has to be stored on the source device that cares about it
  Intermediate nodes do not need any route storage for that destination
    Cost is extra bytes used in each packet for route
During discovery, all paths are returned by destination
  So source gets a full list of possible route choices

## Slide 82: Tradeoffs for reactive routing
Upside: no transmissions unless there is demand
  Routes might appear, disappear, reappear, but no need to update if no one actually wants to transmit anything
Downside: large, variable delay when actually sending a packet
  Full RREQ/RREP protocol before data can actually be sent
  Route might have broken at some point
    So data will be sent based on cached information
    RERR will occur
    RREQ/RREP will occur
    Then data will be sent again

## Slide 83: Proactive routing
Alternative to reactive is to know the routes ahead of time
Periodically query for the possible routes in the network
  Save all routes that are important (maybe just all routes?)
  Also redetermine routes whenever topology changes (nodes join/leave)
Upside: when a packet arrives, route to destination is already known
Downside: requires more memory and effort on part of routers
  Wastes some network bandwidth on checking for route changes

## Slide 84: Distance-Vector
Keep routes as “next hops” rather than full routes
  AODV uses this method (DV for Distance Vector)
Can be combined with proactive techniques too
  Each router periodically informs neighbors of its shortest paths to each destination (in terms of hop count)
    Essentially just broadcast your routing table
  Routers choose the best route available
    Old next-hop it was already aware of
    New next-hop through neighbor (with cost of their hops + 1)
  Need to be careful to avoid loops!

## Slide 85: Reliability as a cost metric
Link quality can very from node to node
  Fewest hops might not be the “fastest” or “most reliable” path
ETX: minimize “expected transmissions”
  Measure link quality over time to determine each link’s reliability
A
B
C
D
E
F

## Slide 86: Alternative cost metrics
Spatial reuse
  Prefer transmission on links that do not interfere with each other
  Improves ability to pipeline data through network
  Example: A<->B and E<->F
Energy availability
  Prefer routing through nodes with more remaining available energy
  Prefer wall-powered nodes over battery-powered
Arbitrarily complex combinations possible

## Slide 87: Wireless routing for mesh networks
The simplest routing protocol is a tree-based protocol (e.g. spanning tree)
Tree is suitable for data collection application, a common application in IoT
What are some possible routing metric?
  Hop Count
  Delay
  Reliability
  Energy

## Slide 88: Expected number of transmissions: ETX
ETX (expected transmissions) is a commonly used routing metric
Consider the path A -> B -> C
Packet reception ratio (PRR)
  A -> B is 0.8, ETX = 1/0.8 = 5/4
  B -> C is 0.5, ETX = 1/0.5 = 2
  Path ETX (A -> B -> C) is 5/4 + 2 = 13/4
A
B
C

## Slide 89: Performing routing using the shortest path
Many practical routing algorithms are based on the notion of shortest path between two nodes
  Each link is assigned a positive number called its length
  A shortest path routing algorithm routes each packet along the minimum length (or shortest) path between the source and destination
  If length is always 1, then shortest path becomes minimum hop routing
  By defining the length using other metrics like cost, delay etc, other paths can be obtained

## Slide 90: Mobile wireless nodes: Ad-hoc wireless routing
What if the nodes are not static but mobile?
A Mobile Ad hoc Network (MANET) is an autonomous system of mobile nodes (MSs) (also serving as routers) connected by wireless links
No infrastructure exists in a MANET
The network’s wireless topology may change dynamically in an unpredictable manner since nodes are free to move and each node has limited transmitting power
Assumption: Due to node mobility, routing path may be available but needs to be “discovered”

## Slide 91: Classification of Ad-hoc routing protocols
The existing routing protocols can be classified as:
  Proactive: when a packet needs to be forwarded, the route is already known
  Reactive: Determine a route only when there is data to send
Routing protocols may also be categorized as:
  (Proactive) Table Driven protocols
  (Reactive) Source Initiated (on demand) protocols

## Slide 92: Delay Tolerant Network (DTN)
(Mobile) Nodes are mostly disconnected
  Range is relatively short. Mobile nodes meet one another opportunistically
  Nodes are mostly in “sleep” mode to conserve power
Typically, to improve delivery ratio, messages are duplicated to many (if not all) nodes
  Improve performance by estimating contact probabilities
Constraints are:
  Number of messages buffered
  Contact duration

## Slide 93: DTN
Some Examples
  Terrestrial Mobile Networks: e.g. bus network
  Exotic Media Networks, e.g. deep space network
  Military Ad-Hoc Networks
  Sensor/Actuator Networks

## Slide 94: Epidemic (Vahdat 2000)
Epidemic – sends all the packet to every node one encounters
Claim: Epidemic routing has the best performance but highest overhead
  True or False?
Enhancement:
  Only relay a message up to x-hops from the source
  Use ACK message to remove delivered messages from buffer

## Slide 95: Single Copy (Spyropoulos, 2004)
Default is for the source to keep the message and only transmit to destination if the two nodes are in direct contact
Relay the message to another node with probability p
  Does this work better?

## Slide 96: Many More Possibilities …
Duplicate a few copies instead of using only one
  Problem: How many copies do we need?
How should contact probabilities be estimated?
  Example 1: Selects next hop based on time of last encounter, transmits to nodes that encounter destination nodes more recently than itself
  Example 2: Records last contact information, e.g. location and time, duplicates messages to nodes which are closer to destination

## Slide 97
Sensor Networking (IoT) Routing

## Slide 98: Routing for constrained internet of things devices
It is similar to mesh routing, design for static, connected network
What are the issues that are important to IoT:
  Energy efficiency, duty cycling

## Slide 99: Link and Neighborhood Management
In a wireless environment, each node needs to decide if a link (to another node) is available.
  Why?
How can this decision be made?
  Usually through some form of measurements
  A node sends beacon and other nodes check if the beacon can be received

## Slide 100: What to measure?
PRR – Packet Reception Ratio
RSSI – Received Signal Strength Indicator
Kannan Srinivasan and Philip Levis, “RSSI is Under Appreciated,” EmNets 2006.

## Slide 101: Measuring Low-Power Wireless Link Quality
To measure PRR,
  Receiver assumes that a transmitter sends S packets over a given period of time T sec
  In T sec, record the number of packets received from transmitter, let this be R
  PRR = R/S
Example:
  T = 1sec, S=100 (if R=95, PRR=0.95)
  T= 10sec, S=100 (if R=55, PRR=0.55)
  T= 100s, S=10 (if R=8, PRR=0.8)

## Slide 102: Measuring Low-Power Wireless Link Quality
Trade-off between communication cost and reaction time
Assume ZigBee radio is used (250Kbps), each transmission takes 1ms (~250bits, ~30bytes) and link measurement probes should not collide
If T=1s, S=100
  Measurement takes up 10% of bandwidth 1 node
  If there are 10 nodes, 100 probes need to be transmitted in 1 sec (100% of bandwidth used only for measurement!)
If T=100s, S=10
  Measurement takes up very little bandwidth
  Is S too small?
  If there is a change in link quality, how long does it take to notice?
    What are “good” values for T and S?

## Slide 103: A “Simple” Beacon-Based Protocol
Node broadcasts beacon messages
When a node receives a “HELLO” message from another node, it identifies the latter as one of its inbound neighbors, and it will include the latter in the “I-HEAR-YOU” message and broadcast the message back to the latter. (detection is one-way!)
In response, when a node receives “I-HEAR-YOU” message from another node (i.e., its ID is included in this “I-HEAR-YOU” message), it identifies the latter as an outbound neighbor.
  The two nodes will become both inbound and outbound neighbors for each other, if they can hear each others’ messages from each other
In practice, the “I-HEAR-YOU” message contains the list of inbound neighbors as well as their PRR values, and the “HELLO” message, are often combined into one packet.

## Slide 104: Example
A
C
B
Hello, I am A
Hello, I am B
Hello, I am C
Hello, I am A, I can hear B and C
Hello, I am B, I can hear A
Hello, I am C, I can hear A and B
What if some of these probe packets are not received?

## Slide 105: Low-Power Wireless Link Asymmetry
Usually only symmetry links are used
What is a (sufficiently) good link?

## Slide 106: Who are my neighbors?
In order to reduce memory and computation cost, neighbor table tends to be small (e.g. 6 – 10)
  How many neighbors are sufficient?
  Only keep track of “good” neighbors

## Slide 107: Who are my neighbors?
Possibility of network partition
  Links within each room is good
  The one link between the 2 room is weak
  If all nodes select the best links, there will be no connection between rooms 1 and 2
How do you address this problem?
Room 1
Room 2

## Slide 108: Collection Tree Protocol (2009)
Current default routing protocol in TinyOS
Tested on 12 different testbeds (20 nodes – 310 nodes)
  > 90% delivery rate in all cases
  > 99% in many cases
Some limitations in evaluation
  In testbed evaluation, there is no issue with battery drain
  Power is often set to maximum value
  Deployment tends to be very dense

## Slide 109: CTP
Major subcomponents
  4-bit link estimator
  Datapath validation
  Adaptive beaconing
Addresses the challenges of reducing overhead of neighbor while having fast reaction to link failure

## Slide 110: Data Driven Estimation
Estimation is agile and driven by the ACK-bit (data-driven estimation)
If a out of Ku packets are acknowledged then
If Ku = 5
1.0
1.25
6.0
EWMA

## Slide 111: Data Path Validation
A data packet carries its estimated ETX value to the root
Receiver compares the ETX value of packet received to its own estimated. If the ETX value is smaller, the transmitted topology is stale
Allows detection on the first data packet, rather than waiting for the routing protocol update

## Slide 112: Adaptive Beaconing
Balance the following needs:
  Sends as few beacons as possible (energy efficiency)
  Reacts quickly to topology changes
Do not use periodic beaconing
Starts from a fixed and small interval T0 (minimum interval)
  If there is no “change”, double interval till TH (maximum interval)
  If a change is detected, drops to T0
Change is defined as:
  Receiver sees larger ETX from transmitter
  ETX drops significantly (> 1.5)
  Neighbor ask for update (e.g. a new node joins)

## Slide 113
Flooding

## Slide 114: Flooding is a recreation of broadcasts
Goal: get information to all nodes
  This is the problem of “data dissemination”
Problem: difficult in Mesh topologies
  Packet loss, retransmission delays
Really, the desire for data dissemination is just to broadcast to all nodes
  But broadcast transmissions don’t reach far enough to cover entire mesh

## Slide 115: Glossy: what if we expand broadcast range by having multiple nodes participate?

## Slide 116: Glossy key techniques
Temporally decouple network flooding from application tasks
Exploit synchronous transmissions for fast network flooding

## Slide 117: Synchronous transmissions
Multiple nodes transmit same packet at same time
R can receive packet with high probability if Δ is small
  May even improve probability of reception (more energy at receiver)
500 ns is 1/32 of a symbol for 802.15.4 (chip duration)

## Slide 118: Fast packet propagation in Glossy

## Slide 119: Fast packet propagation in Glossy

## Slide 120: Fast packet propagation in Glossy

## Slide 121: Fast packet propagation in Glossy

## Slide 122: Glossy details
When Glossy starts
  All nodes turn on radios to receive

## Slide 123: Glossy details
Initiator
  Set relay counter in packet, C = 0
  Broadcast packet

## Slide 124: Glossy details
At packet reception:
  Increment relay counter C
  Transmit synchronously (at a fixed period after the reception)

## Slide 125: Glossy details
At packet reception:
  Increment relay counter C
  Transmit synchronously (at a fixed period after the reception)

## Slide 126: Glossy details
Stop rebroadcasting and turn off radio when
  Already transmitted N times
  Networks pick N for reliability/energy tradeoff

## Slide 127: Glossy details
Tslot is constant by design
  Needs to be to make constructive interference work
Beginning of slot (tref) provides synchronization point
  As a bonus, all nodes are synchronized after flooding event

## Slide 128: Glossy implementation
Device must be able to have tight time bounds on rx/tx
  500 ns wiggle room maximum
  Includes receive, processing, transmission
Need to pick an N for reliability

## Slide 129: Application of Glossy: avoid routing altogether
Low-Power Wireless Bus (LWB)
  Federico Ferrari, Zimmerling, Mottola, Thiele. SenSys’12
Use Glossy for all device communication
  Make one broadcast domain (a bus) where all nodes communicate
  Avoids all issues of routing, everything is a broadcast
    Works for unicast, multicast, anycast, and broadcast transmissions
General idea: TDMA Glossy floods
  Synchronization is already given to nodes by Glossy
  One coordinator makes the TDMA schedule

## Slide 130
RPL

## Slide 131: RPL (IETF RFC 6550)
RPL- Routing over Low Power and Lossy Networks – IETF (www.ietf.org › proceedings › slides › slides-94-rtgarea-2)

## Slide 132: RPL
● Distance Vector (DV) protocol
  Requires that a router to inform its neighbors of topology changes periodically
  Each node maintains a vector (table) of minimum distance to every node
● Source Routing Protocol
  Allows a sender of a packet to partially or completely specify the route the packet takes through the network

## Slide 133: RPL
(Directed Acyclic Graph)

## Slide 135: Control Messages
DODAG Information Solicitation (DIS): used to solicit a DODAG Information Object from a RPL node.
DODAG Information Object (DIO) - The DODAG Information Object carries information that allows a node to discover a RPL Instance, learn its configuration parameters, select a DODAG parent set, and maintain the DODAG
  RPL nodes transmit DIOs using a Trickle Timer.
Destination Advertisement Object (DAO): The Destination Advertisement Object (DAO) is used to propagate destination information Upward along the DODAG.
DAO-ACK

## Slide 136
Rank-based data-path validation mechanisms
In Storing mode, the DAO message is unicast by the child to the selected parent(s).
In Non-Storing mode, the DAO message is unicast to the DODAG root.

## Slide 137: Directed Diffusion (Data Centric)
Node (sink) asks for a particular kind of information, but does not know if the information exists or not
  Sends a query to express an interest for specific information
  Neighboring nodes act if they were the sink and forward queries to their neighbors
  Only one copy of interest/query is forwarded
  Flooding or propagation stops when a (source) node can satisfy an interest/query
Source node floods the answer to sink
Sink assumes that the node from which the first reply arrived is also the neighbor on the “shortest” path
  Reinforce path by sending more query on this path

## Slide 138: Directed Diffusion

## Slide 139: Hierarchical Routing in Sensor Networks
The network consists of a Base Station (BS), away from the nodes, through which the end user can access data from the sensor network
BS can transmit with high power
Sensors cannot reply directly to the BS due to their low power constraints, resulting in asymmetric communication.
Nodes transmit only to their immediate cluster head (CH), thus saving energy
Only CH needs to perform additional computation on data (aggregation)
Adjacent cluster members have similar data

## Slide 140
3.1
3.2
Base Station
3
3.3
2
2.1
2.2
2.3
1
1.0.1
1.0.2
1.0.3
1.2.2
1.2
1.2.5
1.2.4
1.2.3
1.2.1
1.1
1.1.3
1.1.4
1.1.5
1.1.1
1.1.2
Simple sensor node
Second Level Cluster Head
First Level Cluster Head

## Slide 141: Directional Antennas for Co-existence on Shared Wireless Spectrum
Notes: Begin by talking about contributions made with directional antennas to allow co-existence on shared spectrum for battery operated NES
This work was done in the firs two and half years of my PhD studies

## Slide 142: Directional Antenna for Sensing and Communication
What is a directional antenna?
Studied extensively in 1-hop networks, e.g., WiFi networks
ESD antennas are feasible, simple and inexpensive
  SPIDA [1,2] - 6 configurable directions, costs < 5 USD
Power consumption of few microwatts!
[1] Erik Ostrom et al. "Evaluation of an electronically switched directional antenna for real-world low-power wireless networks” – REALWSN 2010
[2] Martin Nilsson. “Directional antennas for wireless sensor networks” - 9th Scandinavian Workshop on Wireless Adhoc Networks 2009
Notes: - Talk about what is directional antenna
A Directional antenna radiates or receives greater power in specific directions.
An ESD or Electronically Steerable Directional antennas is a type of diretional antena that allows the electronic control of the direction of maximum antenna gain. One example of ESD antenna is the SPIDA which you can see in the slide. These antennas are feasble, simple and inexpensive. E.g., the SPIDA antenna you see on the slide can be configured to six possible antenna direction and costs only 5 USD to make.
Despite advantages offered by ESD antennas, they have not been widely used for NES. The protocols and insights from other wireless networks cannot be applied to NES as they are usually multihop in nature, and they present very different challenge as compared to 1-hop networks.
One of the reasons was lack of testbed to perform experiments with ESD antenna. Initial part of my phd studies looked at designing testbed of WSN nodes equipped with the SPIDA antenna.
Next we discuss two sensing and communication application we explored with the ESD antenna.

## Slide 143: Bulk Data Transmissions
Traffic pattern of many WSN applications
  Volcano monitoring [1]
  Bridge monitoring [2]
Directional antenna beneficial for such applications
  Increased communication range at no additional energy cost
  Bulk transmission(s) most severely affected by interference
[1] Geoff Werner-Allen et al. "Fidelity and yield in a volcano monitoring sensor network” in OSDI 2016
[2] Kameswari Chebrolu et al. "Brimon: a sensor network system for railway bridge monitoring” in ACM MOBISYS 2008
Notes: Bulk data is traffic pattern for many WSN applications, including for example volcano monitoring or structural health monitoring. The central feature of these applications is that there is large amount of sensed data that is collected and send over multi-hop low-powered wireless links to a powerful sink node for further processing. The directional antennas are beneficial for such applications as they increase the communication range at no additional energy cost, also bulk transmissions as they occupy channel for larger period of time are more severely affected by interference. However, in WSN there are no existing protocol to exploit this.

## Slide 144: DPT’s Contributions
Directional Pipelined Transmissions (DPT)
  Leverage directional transmissions and receptions
  Reduce inter/intra path interference using directional communication
  Highest reported throughput in 802.15.4 multi-hop links
  Operation on single wireless channel
  DPT creates two pipelines between source and sink
    All nodes are always active!
Notes: So our main contribution in this work is we present a protocol called DPT which leverages directional transmissions and receptions. We demonstrate that directional communication can reduce intra/inter path interference signficiantly. We further demontsrate that this reduced interapath and interpath interference allows high throughput multihop transmissions to occur on one wireless channel. We also achieve the highest reported throughput in 802.15.4 multihop links.

## Slide 145: DPT Throughput Comparison
Existing protocols not designed for ESD antennas
State-of-the-art:
  P3 [1] multiple channels ,higher node density
[1] Manjunath Doddavenkatappa et al. "P 3: a practical packet pipeline using synchronous transmissions for wireless sensor networks.” in ACM/IEEE IPSN 2014
Notes: We compare the performance of DPT to the state of the art in bulk forwarding in WSN. Since these existing protocols were not designed for ESD antennas, we do not experimentally compare DPT with thesse protocols. We compare the performance of DPT with the highest reported throughput from their respective publications. As we see on the figure on the screen, DPT out performs all of the protocol in terms of highest throughput achieved for both single path and disjoint path. P3 is closest in terms of performance to DPT, however, unlike P3 we use only one wireless channel for bulk data transmission.

## Slide 146: Learning Objective for Today’s Lecture
Review: last few lecture’s topics
Node Discovery
Routing
IoT/Sensor Network Routing
Flooding
RPL
Misc and Case Study

## Slide 147: Wireless Networking
Ambuj Varshney
Assistant Professor, National University of Singapore
Wireless, Embedded Intelligence, Sensing, and Emerging Technologies Group
ambujv@nus.edu.sg