## Slide 1: Wireless Networking (CS4222 / 5422) Tutorial - 7
TA: Malaika
Email Id: mafra@comp.nus.edu.sg

## Slide 2: Q1. A node running BMAC spends its time in 4 states – (1) sleeping, (2) idle listening (3) receiving and (4) transmission. By default, it wakes up every 250ms to sample the channel for a duration of 5ms. Every 5s, each node transmits/receives with equal probability. Packet transmission or reception duration is always 5ms.
Idle Listening
…
Transmitting
Preamble
Data
250 ms
5 ms
(250 + 5) ms
Sleeping
Receiving
Data
…
~ (125 + 5) ms
a) On average, what % of the energy is spent in the four states?
Preamble

## Slide 3
Idle Listening
Cycle
…
Transmitting
Cycle
Preamble
Data
250 ms
5 ms
(250 + 5) ms
Sleeping
Receiving
Cycle
Preamble
Data
…
~ (125 + 5) ms
a) On average, what % of the energy is spent in the four states?
State | Power
Sleep | 1mW
Idle Listen | 10mW
Receive | 20mW
Transmit | 20mW
Idle Listening Cycle Duration = 245ms (sleep) + 5ms (idle listen)
Receiving Cycle Duration
= 125ms (sleep) + 125ms (idle listen) + 5ms (receive)
= 255ms
Transmitting Cycle Duration
= 250ms + 5ms (transmit)
What % of all cycles are in idle listening, receive and transmit cycles?
In 5.005s, we have a total of 20 cycles (i.e., 5s/250ms)
19 cycles in idle listening, 1 cycle in TX/RX
95% idle, 2.5% TX, 2.5% RX

## Slide 4
Idle Listening
Cycle
…
Transmitting
Cycle
Preamble
Data
250 ms
5 ms
(250 + 5) ms
Sleeping
Receiving
Cycle
Preamble
Data
…
~ (125 + 5) ms
a) On average, what % of the energy is spent in the four states?
State | Power
Sleep | 1mW
Idle Listen | 10mW
Receive | 20mW
Transmit | 20mW
Energy spent in sleep state during Idle Listening Cycle
= 245ms X 1mW = 245e-3 mJ
Energy spent in sleep state during RX Cycle
= 125ms X 1mW = 125e-3 mJ
Energy spent in sleep state during TX Cycle
= 0 J
Total Energy/cycle in Sleep State
= 0.95 X 245e-3 + 0.025 X 125e-3 + 0.025 X 0
= 0.2358 mJ/cycle

## Slide 5
Idle Listening
Cycle
…
Transmitting
Cycle
Preamble
Data
250 ms
5 ms
(250 + 5) ms
Sleeping
Receiving
Cycle
Preamble
Data
…
~ (125 + 5) ms
a) On average, what % of the energy is spent in the four states?
State | Power
Sleep | 1mW
Idle Listen | 10mW
Receive | 20mW
Transmit | 20mW
Energy spent in idle state during Idle Listening Cycle
= 5ms X 10mW = 50e-3 mJ
Energy spent in idle state during RX Cycle
= 125ms X 10mW = 1.25 mJ
Energy spent in idle state during TX Cycle
= 0 J
Total Energy in Idle State (mJ/cycle )
= 0.95 X 50e-3 + 0.025 X 1.25 + 0.025 X 0
= 0.07875 mJ/cycle

## Slide 6
Idle Listening
Cycle
…
Transmitting
Cycle
Preamble
Data
250 ms
5 ms
(250 + 5) ms
Sleeping
Receiving
Cycle
Preamble
Data
…
~ (125 + 5) ms
a) On average, what % of the energy is spent in the four states?
State | Power
Sleep | 1mW
Idle Listen | 10mW
Receive | 20mW
Transmit | 20mW
Energy spent in RX state during Idle Listening Cycle
= 0 J
Energy spent in RX state during RX Cycle
= 5ms X 20mW = 100e-3 mJ
Energy spent in RX during TX Cycle
= 0 J
Total Energy in Rx State (mJ/cycle)
= 0.025 X 0.1
= 0.0025 mJ/cycle

## Slide 7
Idle Listening
Cycle
…
Transmitting
Cycle
Preamble
Data
250 ms
5 ms
(250 + 5) ms
Sleeping
Receiving
Cycle
Preamble
Data
…
~ (125 + 5) ms
a) On average, what % of the energy is spent in the four states?
State | Power
Sleep | 1mW
Idle Listen | 10mW
Receive | 20mW
Transmit | 20mW
Energy spent in TX state during Idle Listening Cycle
= 0 J
Energy spent in TX state during RX Cycle
= 0 J
Energy spent in TX state during TX Cycle
= 255ms X 20mW = 0.510mJ
Total Energy in Tx State (mJ/cycle)
= 0.025 X 0.510
= 0.1275 mJ/cycle

## Slide 8
Idle Listening
Cycle
…
Transmitting
Cycle
Preamble
Data
250 ms
5 ms
(250 + 5) ms
Sleeping
Receiving
Cycle
Preamble
Data
…
~ (125 + 5) ms
a) On average, what % of the energy is spent in the four states?
State | Power
Sleep | 1mW
Idle Listen | 10mW
Receive | 20mW
Transmit | 20mW
State | Total Energy per State (mJ/cycle ) | % of Total Energy
Sleep | 0.2358 | 53% = 0.2358/0.4446
Idle Listening | 0.07875 | 17.7%
RX | 0.0025 | 0.56%
TX | 0.1275 | 28.7%
Total | 0.4446 | 

## Slide 9
b) If the battery used provides 10KJ of energy, what is the lifetime of the node?
State | Total Energy per State (mJ / cycle) | % of Total Energy
Sleep | 0.2358 | 53.1% = 0.2358/0.4446
Idle Listening | 0.07875 | 17.7%
RX | 0.0025 | 0.56%
TX | 0.1275 | 28.7%
Total | 0.4446 | 
Avg energy per cycle = 0.4446 mJ/cycle
But, we know 20 cycles  5.005s
Hence, avg power per sec = (0.4446 X 20)/5.005 = 1.777mJ/s = 1.777mW
Hence,
Lifetime of the node = 10kJ / 1.777mW = 5.63e6 seconds 65 days

## Slide 10: Q2. The per-hop packet error rate on a path with four hops are 0.25, 0.1, 0.5, and 0.2. What is the (a) path ETX and (b) the probability that a packet can traverse the path with no error/retransmission?
A
B
C
D
E
Packet
Error Rate
0.25
0.1
0.5
0.2
Packet
Reception Rate
0.75
0.9
0.5
0.8

## Slide 11: Q2. The per-hop packet error rate on a path with four hops are 0.25, 0.1, 0.5, and 0.2. What is the (a) path ETX and (b) the probability that a packet can traverse the path with no error/retransmission?
A
B
C
D
E
Packet
Reception Rate
0.75
0.9
0.5
0.8
ETX = (1/0.75) + (1/0.9) + (1/0.5) + (1/0.8)
= 5.69

## Slide 12: Q2. The per-hop packet error rate on a path with four hops are 0.25, 0.1, 0.5, and 0.2. What is the (a) path ETX and (b) the probability that a packet can traverse the path with no error/retransmission?
A
B
C
D
E
Packet
Reception Rate
0.75
0.9
0.5
0.8
No error  Successful transmission in every hop
P(no error) = 0.75 x 0.9 x 0.5 x 0.8 = 0.27

## Slide 13: Q3. In the figure below, nodes indicate IoT devices and two nodes can communicate if there is a link between them. The number associated with each link is the link quality measured in expected packet delivery ratio.
0
1
2
3
4
5
0.9
0.8
0.9
1.0
0.9
0.9
0.8
0.6

## Slide 14: Q3(a) Find the shortest path from node 5 to node 0 using two different routing metric: Hop count
0
1
2
3
4
5
0.9
0.8
0.9
1.0
0.9
0.9
0.8
0.6
Path with hop count = 1?
  Does not exist!
Path with hop count = 2?
  Exists! 5  1  0

## Slide 15: Q3(b) Find the shortest path from node 5 to node 0 using two different routing metric: ETX
0
1
2
3
4
5
0.9
0.8
0.9
1.0
0.9
0.9
0.8
0.6
Path 5  1  0
  ETX = (1/0.6) + (1/0.9) = 2.77

## Slide 16: Q3(b) Find the shortest path from node 5 to node 0 using two different routing metric: ETX
0
1
2
3
4
5
0.9
0.8
0.9
1.0
0.9
0.9
0.8
0.6
Path 5  1  0
  ETX = (1/0.6) + (1/0.9) = 2.77
Path 5  3  1  0
  ETX = (1/0.8) + (1/0.8) + (1/0.9) = 3.61

## Slide 17: Q3(b) Find the shortest path from node 5 to node 0 using two different routing metric: ETX
0
1
2
3
4
5
0.9
0.8
0.9
1.0
0.9
0.9
0.8
0.6
Path 5  1  0
  ETX = (1/0.6) + (1/0.9) = 2.77
Path 5  3  1  0
  ETX = (1/0.8) + (1/0.8) + (1/0.9) = 3.61
Path 5  3  2  0
  ETX = (1/0.8) + (1/1) + (1/0.9) = 3.36

## Slide 18: Q3(b) Find the shortest path from node 5 to node 0 using two different routing metric: ETX
0
1
2
3
4
5
0.9
0.8
0.9
1.0
0.9
0.9
0.8
0.6
Path 5  1  0
  ETX = (1/0.6) + (1/0.9) = 2.77
Path 5  3  1  0
  ETX = (1/0.8) + (1/0.8) + (1/0.9) = 3.61
Path 5  3  2  0
  ETX = (1/0.8) + (1/1) + (1/0.9) = 3.36
Path 5  4  2  0
  ETX = (3/0.9) = 3.33

## Slide 19: Q3(b) Find the shortest path from node 5 to node 0 using two different routing metric: ETX
0
1
2
3
4
5
0.9
0.8
0.9
1.0
0.9
0.9
0.8
0.6
Path 5  1  0
  ETX = (1/0.6) + (1/0.9) = 2.77
Path 5  3  1  0
  ETX = (1/0.8) + (1/0.8) + (1/0.9) = 3.61
Path 5  3  2  0
  ETX = (1/0.8) + (1/1) + (1/0.9) = 3.36
Path 5  4  2  0
  ETX = (3/0.9) = 3.33
Path 5  4  2  3  1  0
  ETX = (3/0.9) + 1/0.8 + 1/1 = 5.58
BEST ETX

## Slide 20: Q3(c) Let the minimum usable link quality be set to 0.6. If the shortest hop count is X, what is the ETX in terms of X?
A
B
C
D
E
Packet
Reception Rate
>= 0.6
>= 0.6
>= 0.6
>= 0.6
ETX = (1/0.6) + (1/0.6) + … X times
= X/0.6 = 5X/3

## Slide 21: Q4. What are (1) wireless mesh network, (2) mobile ad hoc network and (3) delay/disruption tolerant network? What are the differences in the design of the respective routing protocols for each of these 3 different types of networks?
Wireless Mesh Network
  Constraints : Static nodes
  Routing protocols : Select routes that minimize interference
  Advantages : Offers redundancy in case of node failures
  Examples : Electric smart meters

## Slide 22: Q4. What are (1) wireless mesh network, (2) mobile ad hoc network and (3) delay/disruption tolerant network? What are the differences in the design of the respective routing protocols for each of these 3 different types of networks?
Mobile Ad-hoc Network
  Challenges : nodes are mobile, no pre-existing infrastructure,
  Routing protocols : Every node participates in routing - Proactive / Reactive
  Examples : sensor networks

## Slide 23: Q4. What are (1) wireless mesh network, (2) mobile ad hoc network and (3) delay/disruption tolerant network? What are the differences in the design of the respective routing protocols for each of these 3 different types of networks?
Delay-tolerant network
  Challenges : lack of continuous end-to-end connectivity, sparsity of nodes, limited radio range
  Routing protocols : store-and-forward approach, requires sufficient local storage at nodes
  Examples : Military Ad-hoc network